PART IV:                                                                         Landtype Associations Management Applications

This section contains lists of properties, hazard ratings, limitations or suitability for management consideration, and potential response to natural disturbance.  Properties are developed from field observation and aerial photo interpretation.  Properties are listed on order of their dominance or importance to major ecological processes in a Landtype Association (LTA).  Ratings are relative to each other and are derived mostly from empirical interpretation of dominant processes identified with each Landtype Association and field observation.  Suitability for management and limitations to management are based upon referenced criteria and conditions that present potential degradation or increased cost in development to avoid degradation.  Potential responses to natural disturbances are extrapolated from research literature by applying regionally or nationally recognized classification systems to processes identified for each Landtype Association.  Narrative sections prior to interpretation tables contain definitions, sources, and clarifications important to understanding the qualification of the interpretation.  It is important to read these sections prior to using the interpretation tables.

The same information is available in digital format with the map coverage in ARCGIS environment.  A series of databases (using ACCESS) can be formatted to make tables suited to user needs and for only the LTAs of interest.  Tables in this report provide information in subject areas most commonly needed by most users, but most importantly, documents the basis for the interpretations.

There are many uses for this information.  Table 7 lists geomorphic processes in order of occurrence and provides a general summary of physical features needed for more general types of analysis.  This is useful to those seeking a basic understanding of landform genesis and to compare basic LTA concepts.  Table 8 identifies representative soil components for each LTA and their physical properties, and provides a more detailed look at the variation of physical properties within each LTA.  Tables 9 and 10 provide interpretations useful to understanding watershed processes and information that assists in rating relative risk to watersheds from management activities or natural disturbance.  Table 11 provides information relative to wildlife and fisheries habitats useful to landscape analysis.  Table 12 and Table 13 provide information useful in vegetation management including productivity interpretations and suitability for use in timber and grazing management.

Landtype Association Geomorphic Processes and General Physical Properties

Table 7 contains a list of dominant geomorphic processes, both relic and active, that influenced landforms and surficial properties, as they exist today.  Other general physical properties are summarized for each LTA.  These summaries are provided for users interested in a brief overview of geomorphic differences between Landtype Associations.  The information is an aggregate of the more detailed information by soil component that is contained in Table 8, Soil Classification and Properties.

Landform:  This column lists the landform group name for the Landtype Association.  A narrative description is provided in Section II.

Dominant Bedrock:  This column lists the most commonly occurring bedrock for each Landtype Association.  Not all combinations of differentia occur with all map criteria and this column identifies which bedrock most commonly occurs with the other map differentia for a particular Landtype Association.  Undifferentiated is used where the distinction was not made for surficial deposits originating from any number of kinds of bedrock materials.

Relict and Active Geomorphic Processes:  These two columns list the geomorphic processes as identified using A Geomorphic Classification System (Haskins et al 1996).  The nomenclature is as closely matching this reference as possible but not exactly.  Subprocesses within major processes are too complex to discern at the Landtype Association scale.  Relic processes are those that have occurred in the geologic past but are continuing to influence geomorphic processes through landform shape, landscape position, and soil development.  These processes are listed in order of time sequence with the oldest being listed first.  Only the major relic land-forming processes continuing to influence active processes are listed. Active processes are listed in order of time sequence and dominance.  Time sequence of distinct and separate processes are separated by a slash (/) whereas those processes that may be related or resultant from another process are separated by an “and”.  A comma ( , ) separation denotes that the processes may occur concurrently or sequentially.

Slope Gradient:  This column contains an average range or dominant slope gradient range in percent of each map unit.  Exceptions will occur within the map unit but are expected to be of minor extent.

Volcanic Ash:  This column lists four of the five classes of volcanic ash mantle: thick mantle, thin mantle, mixed ash, and no ash or no influence.  Minor ash class is of lesser extent and was combined with mixed ash for this table.  Entries in this column are a summary of the variation for the entire map unit.  For extent of all the classes within an LTA, consult Table 8, Soil Classification and Properties.

Distribution of volcanic ash serves as an index to erosion, deposition, fire frequency, cover by vegetation and litter, and general landscape stability.  Thicker layers indicate more stable or depositional environments while thinner layers indicate erosional environments and possibly higher fire frequency.  And, generally, distribution, depth, and ash disturbance (i.e. mixing) are correlated with slope gradient, slope position, and slope aspect.  Thick, undisturbed ash mantles  occur on north aspects and mid to higher elevation gentle slopes and support moist forest.  Although of minor extent in the landscape, ash deposits, ten or more feet thick,  remain on protected landscape segments along toeslopes of steep mountain slopes and plateau scarps.  Drifts, flows, avalanches and slides of ash; energized by wind, water and gravity accumulated ash into these spectacular deposits.  Mounds of volcanic ash, redistributed by wind commonly occur on backslopes of plateaus and are less common on plateau summits.  Mixed ash occurs on colluvial foot slopes, climatic zones with more frequent fire and areas that receive significant loess deposition.  Soil materials in flood plains and low terraces on valley floors are devoid of ash having been washed away by floods since ash was deposited.

The following classes define the amount or influence  of volcanic ash for each LTA.

Ash mantles (>60 percent volcanic ash; >7 inches thick)

Thick (> 14 inches thick)

Thin (7-14 inches thick)

Mixed ash (30-60 percent volcanic ash; >7 inches thick)

No ash influence (0-5 percent volcanic ash)

Regolith Texture:  Regolith texture is of the unconsolidated material from the base of the surface layer to a bedrock contact.  In the case of regoliths with ash mantles, the regolith texture may be vastly different that the surface texture.  Ash mantle textures fall within the medium textural class.  Textures are grouped using the Soil Textural Classes defined in the USDA Soil Survey Manual (USDA Soil Survey 1993).

Soil Textural Classes are as follows:

coarse -  sands and loamy sands

moderately coarse - sandy loams

medium - very fine sands, loams, silt loams, and silt

moderately fine - clay loams, sandy clay loams, and silty clay loams

fine-  sandy clay, silty clay, and clay

Depth to Bedrock:  This column contains the average range of depth to hard bedrock based upon soil descriptions from the Landtype (TEUI) inventory and empirical interpretation of exceptions that are anticipated to occur.  For more detail about extent of the various soil depths for a LTA, consult Table 7.

Table 7.  Landtype Association Geomorphic Processes and General Physical Properties

| LTA | Landform | Dominant Bedrock | Relict Geomorphic Process | Active Geomorphic _Process | Slope Gradient (%) | Volcanic Ash | Regolith Texture | Depth to Bedrock |
| --- | --- | --- | --- | --- | --- | --- | --- | --- |
| 114 | Landslides | Basalt | Lava Flow/Uplift/Eolian | Landslide | 30 to 60 | thick | medium | 3-20 |
| 115 | Basins, Fans, and Terraces | Basalt | Lava Flow/Uplift/Eolian | Fluvial and Pluvial Erosion/Deposition | 15 to 50 | thick | medium | 3-10 |
| 116 | Mountain Slopes, Gentle | Basalt | Lava Flow/Uplift/Eolian | Pluvial and Wind Erosion | 0 to 30 | thick | medium | 2-5 |
| 117 | Mountain Slopes, Steep | Basalt | Lava Flow/Uplift/Eolian | Fluvial and Colluvial Erosion | 30 to 60 | thick | medium | 3-20 |
| 118 | Canyons | Basalt | Lava Flow/Uplift/Eolian | Fluvial, Mass Wasting, and Colluvial Erosion | 60 to 90 | thick & mixed | medium to moderately fine | <1-10 |
| 124 | Land Slide | Volcanic tuffs and lakebed clays | Pyroclastic Flow/Uplift/Eolian | Landslide | 0 to 60 | thick | moderately fine to fine | 2-20 |
| 125 | Basins, Fans, and Terraces | Volcanic tuffs and lakebed clays | Pyroclastic Flow/Uplift/Eolian | Fluvial and Pluvial Erosion/Deposition | 15 to 50 | thick | moderately fine to fine | 3-10 |
| 126 | Mountain Slopes, Gentle | Volcanic tuffs and lakebed clays | Pyroclastic Flow/Uplift/Eolian | Pluvial and Wind Erosion | 0 to 30 | thick | moderately fine to fine | 2-10 |
| 127 | Mountain Slopes, Steep | Volcanic tuffs and lakebed clays | Pyroclastic Flow/Uplift/Eolian | Fluvial and Colluvial Erosion | 30 to 60 | thick | fine to moderately fine | 2-5 |
| 131 | Trough Floors | Undifferentiated | Glaciation/Glacial Deposition/Eolian | Fluvial Erosion | 10 to 50 | thick | moderately coarse | 3-20 |
| 132 | Trough Walls, Cirques, & Alpine Ridges | Undifferentiated | Glaciation/Glacial Erosion/Eolian | Fluvial, Mass Wasting, Colluvial Erosion | 10 to 90 | thick | moderately coarse | 0-10 |
| 133 | Alluvial Valley Floors | Undifferentiated | Tectonic Faulting/Eolian/Stream Processes | Fluvial Erosion/Deposition | 0 to 15 | no influence & thick | moderately coarse to moderately fine | >20 |
| 135 | Basins, Fans, and Terraces | Undifferentiated | Undifferentiated/Eolian/ Fluvial/MassWasting/Eolian | Mass Wasting/Fluvial Erosion and Deposition | 15 to 50 | no influence & thick | moderately fine to moderately coarse | 10-20 |
| 144 | Land Slide | Basalt interlayed with lacustrine sediments | Lacustrine/Volcanic Flow/Eolian | Landslide | 0 to 60 | thick | moderately fine to fine | 3-20 |
| 146 | Mountain Slopes, Gentle | Basalt interlayed with lacustrine sediments | Lacustrine/Volcanic Flow/Eolian | Pluvial and Wind Erosion, Landslide | 0 to 30 | thick | medium to fine | 3-10 |
| 155 | Basins, Fans, and Terraces | Rhyolitic tuff, Granite, Gneiss/Schist. | PyroclasticFlows and IgneousIntrusives/Uplift/Eolian | Fluvial and Pluvial Erosion/Deposition | 15 to 50 | thick | medium | 3-5 |
| 156 | Mountain Slopes, Gentle | Rhyolitic tuff, Granite, Gneiss/Schist. | PyroclasticFlows and IgneousIntrusives/Uplift/Eolian | Pluvial and Wind Erosion | 0 to 30 | thick | moderately coarse | 3-5 |
| 157 | Mountain Slopes, Steep | Rhyolitic tuff, Granite, Gneiss/Schist. | PyroclasticFlows and IgneousIntrusives/Uplift/Eolian | Fluvial and Colluvial Erosion | 30 to 60 | thick | moderately coarse | 3-5 |
| 158 | Canyons | Rhyolitic tuff, Granite, Gneiss/Schist. | PyroclasticFlows and IgneousIntrusives/Uplift/Erosion/Eolian | Fluvial and Colluvial Erosion | 60 to 90 | thick & mixed | moderately coarse to coarse | 2-5 |
| 165 | Basins, Fans, and Terraces | Metavolcanic, Metasedimentary, Serpentine | Tectonic Folding/Uplift/Eolian | Fluvial and Pluvial Erosion/Deposition | 15 to 50 | thin & thick | moderately coarse to medium | 2-10 |
| 166 | Mountain Slopes, Gentle | Metavolcanic, Metasedimentary, Serpentine | Tectonic Folding/Uplift/Eolian | Pluvial and Wind Erosion | 0 to 30 | thin & thick | moderately coarse to medium | 2-3 |
| 167 | Mountain Slopes, Steep | Metavolcanic, Metasedimentary, Serpentine | Tectonic Folding/Uplift/Eolian | Fluvial and Colluvial Erosion | 30 to 60 | thick & mixed | moderately fine to moderately coarse | 3-10 |
| 168 | Canyons | Metavolcanic, Metasedimentary, Serpentine | Tectonic Folding/Uplift/Eolian | Fluvial, Mass Wasting, and Colluvial Erosion | 60 to 90 | thick & mixed | moderately fine to moderately coarse | 2-10 |
| 176 | Mountain Slopes, Gentle | Sedimentary Sandstones | Tectonic-Undiff./Uplift/Eolian | Pluvial and Wind Erosion | 0 to 30 | mixed | medium to moderately fine | <1-3 |
| 177 | Mountain Slopes, Steep | Sedimentary Sandstones | Tectonic-Undiff./Uplift/Eolian | Fluvial and Colluvial Erosion | 30 to 60 | thick & mixed | moderately fine to medium | <1-5 |
| 214 | Land Slide | Basalt | Lava Flow/Uplift/Eolian | Landslide | 0 to 60 | mixed | fine to moderately fine | 3-10 |
| 215 | Basins, Fans, and Terraces | Basalt | Lava Flow/Uplift/Eolian | Fluvial and Pluvial Erosion/Deposition | 15 to 50 | mixed | moderately fine | 2-5 |
| 216 | Mountain Slopes, Gentle | Basalt | Lava Flow/Uplift/Eolian | Pluvial and Wind Erosion | 0 to 30 | mixed | moderately fine to medium | 2-5 |
| 217 | Mountain Slopes, Steep | Basalt | Lava Flow/Uplift/Eolian | Fluvial and Colluvial Erosion | 30 to 60 | mixed | moderately fine to medium | 3-10 |
| 218 | Canyons | Basalt | Lava Flow/Uplift/Erosion/ Eolian | Fluvial, Mass Wasting, and Colluvial Erosion | 60 to 90 | mixed | moderately fine to medium | <1-5 |
| 224 | Land Slide | Volcanic tuffs and lakebed clays | Pyroclastic Flow/Uplift/Eolian | Landslide | 0 to 60 | mixed and thin | fine to moderately fine | 3-20 |
| 226 | Mountain Slopes, Gentle | Volcanic tuffs and lakebed clays | Pyroclastic Flow/Uplift/Eolian | Pluvial and Wind Erosion | 0 to 30 | mixed | moderately fine to fine | 2-5 |
| 227 | Mountain Slopes, Steep | Volcanic tuffs and lakebed clays | Pyroclastic Flow/Uplift/Eolian | Fluvial and Colluvial Erosion | 30 to 60 | mixed | moderately fine to fine | 2-5 |
| 231 | Trough Floors | Undifferentiated | Glaciation/Glacial Deposition/Eolian | Fluvial Erosion | 10 to 50 | thick & mixed | moderately coarse | 3-20 |
| 232 | Trough Walls, Cirques, & Alpine Ridges | Undifferentiated | Glaciation/Glacial Erosion/Eolian | Fluvial, Mass Wasting, Colluvial Erosion | 10 to 90 | thick & mixed | moderately coarse | 0-20 |
| 233 | Alluvial Valley Floors | Undifferentiated | Tectonic Faulting/Eolian/Stream Processes | Fluvial Erosion/Deposition | 0 to 15 | mixed and thin | moderately fine to medium | >20 |
| 236 | Mountain Slopes, Gentle | Undifferentiated | Tectonic Uplift/Eolian/Stream Processes | Fluvial Erosion/Deposition | 0 to 30 | mixed and thin | moderately fine to medium | >20 |
| 244 | Land Slide | Basalt interlayed with lacustrine sediments | Lacustrine/Volcanic Flow/Eolian | Landslide | 0 to 60 | mixed | fine to moderately fine | 2-10 |
| 246 | Mountain Slopes, Gentle | Basalt interlayed with lacustrine sediments | Lacustrine/Volcanic Flow/Eolian | Pluvial and Wind Erosion, Landslide | 0 to 30 | mixed | fine to moderately fine | 2-5 |
| 256 | Mountain Slopes, Gentle | Rhyolitic tuff, Granite, Gneiss/Schist. | PyroclasticFlows and IgneousIntrusives/Uplift/Eolian | Pluvial and Wind Erosion | 0 to 30 | thick & mixed | medium | 2-5 |
| 257 | Mountain Slopes, Steep | Rhyolitic tuff, Granite, Gneiss/Schist. | PyroclasticFlows and IgneousIntrusives/Uplift/Eolian | Fluvial and Colluvial Erosion | 30 to 60 | thick & mixed | moderately fine to medium | 3-5 |
| 258 | Canyons | Rhyolitic tuff, Granite, Gneiss/Schist. | PyroclasticFlows and IgneousIntrusives/Uplift/ Erosion/Eolian | Fluvial, Mass Wasting, and Colluvial Erosion | 60 to 90 | mixed | medium | 1-5 |
| 265 | Basins, Fans, and Terraces | Metavolcanic, Metasedimentary, Serpentine | Tectonic Folding/Uplift/Eolian | Fluvial and Pluvial Erosion/Deposition | 15 to 50 | mixed and thin | moderately coarse | 2-20 |
| 266 | Mountain Slopes, Gentle | Metavolcanic, Metasedimentary, Serpentine | Tectonic Folding/Uplift/Eolian | Pluvial and Wind Erosion | 0 to 30 | mixed | moderately fine to medium | <1-3 |
| 267 | Mountain Slopes, Steep | Metavolcanic, Metasedimentary, Serpentine | Tectonic Folding/Uplift/Eolian | Fluvial and Colluvial Erosion | 30 to 60 | mixed and thin | medium to moderately coarse | 2-10 |
| 268 | Canyons | Metavolcanic, Metasedimentary, Serpentine | Tectonic Folding/Uplift/Eolian | Fluvial, Mass Wasting, and Colluvial Erosion | 60 to 90 | mixed and thin | medium | <1-3 |
| 273 | Alluvial Valley Floors | Sedimentary Sandstones | Tectonic Faulting/Eolian/Stream Processes | Fluvial Erosion/Deposition | 0 to 15 | no influenced and mixed | medium to moderately fine | <1-5 |
| 275 | Basins, Fans, and Terraces | Sedimentary Sandstones | Tectonic-undiff/Fluvial/Mass Wasting/Eolian | Mass Wasting/Fluvial Erosion and Deposition | 15 to 50 | mixed | medium | <1-3 |
| 276 | Mountain Slopes, Gentle | Sedimentary Sandstones | Tectonic-Undiff./Uplift/Eolian | Pluvial and Wind Erosion | 0 to 30 | mixed | moderately fine to medium | <1-3 |
| 277 | Mountain Slopes, Steep | Sedimentary Sandstones | Tectonic-Undiff./Uplift/Eolian | Fluvial and Colluvial Erosion | 30 to 60 | mixed | moderately fine to medium | <1-5 |
| 315 | Basins, Fans, and Terraces | Basalt | Lava Flow/Uplift/Eolian | Fluvial and Pluvial Erosion | 15 to 50 | mixed | moderately coarse to medium | 2-5 |
| 316 | Mountain Slopes, Gentle | Basalt | Lava Flow/Uplift/Eolian | Pluvial and Wind Erosion | 0 to 30 | mixed | medium | <1-2 |
| 317 | Mountain Slopes, Steep | Basalt | Lava Flow/Uplift/Eolian | Fluvial and Colluvial Erosion | 30 to 60 | mixed | medium | <1-3 |
| 318 | Canyons | Basalt | Lava Flow/Uplift/Erosion/ Eolian | Fluvial, Mass Wasting, and Colluvial Erosion | 60 to 90 | mixed | medium | <1-3 |
| 326 | Mountain Slopes, Gentle | Volcanic tuffs and lakebed clays | Pyroclastic Flow/Uplift/Eolian | Pluvial and Wind Erosion | 0 to 30 | mixed | fine | <1-3 |
| 327 | Mountain Slopes, Steep | Volcanic tuffs and lakebed clays | Pyroclastic Flow/Uplift/Eolian | Fluvial and Colluvial Erosion | 30 to 60 | mixed | fine | <1-3 |
| 332 | Trough Walls, Cirques, & Alpine Ridges | Undifferentiated | Glaciation/Glacial Erosion/Eolian | Fluvial, Mass Wasting, Colluvial Erosion | 10 to 90 | mixed | moderately coarse to coarse | 0-10 |
| 333 | Alluvial Valley Floors | Undifferentiated | Tectonic Faulting/Eolian/Stream Processes | Fluvial Erosion/Deposition | 0 to 15 | mixed | moderately fine to fine | >20 |
| 356 | Mountain Slopes, Gentle | Rhyolitic tuff, Granite, Gneiss/Schist. | PyroclasticFlows and IgneousIntrusives/Uplift/Eolian | Pluvial and Wind Erosion | 0 to 30 | no influence and mixed | moderately coarse | <1-2 |
| 357 | Mountain Slopes, Steep | Rhyolitic tuff, Granite, Gneiss/Schist. | PyroclasticFlows and IgneousIntrusives/Uplift/Eolian | Fluvial and Colluvial Erosion | 30 to 60 | no influence and mixed | moderately coarse | <1-10 |
| 358 | Canyons | Rhyolitic tuff, Granite, Gneiss/Schist. | PyroclasticFlows and IgneousIntrusives/Uplift/ Erosion/Eolian | Fluvial, Mass Wasting, and Colluvial Erosion | 60 to 90 | mixed | medium | 0-2 |
| 365 | Basins, Fans, and Terraces | Metavolcanic, Metasedimentary, Serpentine | Tectonic Folding/Uplift/Eolian | Fluvial and Pluvial Erosion/Deposition | 15 to 50 | mixed | medium | <1-2 |
| 366 | Mountain Slopes, Gentle | Metavolcanic, Metasedimentary, Serpentine | Tectonic Folding/Uplift/Eolian | Pluvial and Wind Erosion | 0 to 30 | mixed | medium | <1-2 |
| 367 | Mountain Slopes, Steep | Metavolcanic, Metasedimentary, Serpentine | Tectonic Folding/Uplift/Eolian | Fluvial and Colluvial Erosion | 30 to 60 | thick and thin | moderately coarse | 3-5 |
| 368 | Canyons | Metavolcanic, Metasedimentary, Serpentine | Tectonic Folding/Uplift/Erosion/Eolian | Fluvial, Mass Wasting, and Colluvial Erosion | 60 to 90 | mixed | medium | <1-2 |
| 376 | Mountain Slopes, Gentle | Sedimentary Sandstones | Tectonic-Undiff./Uplift/Eolian | Pluvial and Wind Erosion | 0 to 30 | mixed | medium | <1-2 |
| 377 | Mountain Slopes, Steep | Sedimentary Sandstones | Tectonic-Undiff./Uplift/Eolian | Fluvial and Colluvial Erosion | 30 to 60 | mixed | medium | <1-3 |
| 416 | Mountain Slopes, Gentle | Basalt | Lava Flow/Uplift/Eolian | Pluvial and Wind Erosion | 0 to 30 | mixed | medium | 2-5 |
| 418 | Canyons | Basalt | Lava Flow/Uplift/Eolian | Fluvial, Mass Wasting, and Colluvial Erosion | 60 to 90 | mixed | medium | 2-5 |
| 432 | Trough Walls, Cirques, & Alpine Ridges | Undifferentiated | Glaciation/Glacial Erosion/Eolian | Fluvial, Mass Wasting, Colluvial Erosion | 10 to 90 | mixed | medium | 0-2 |
| 433 | Alluvial Valley Floors | Undifferentiated | Undifferentiated/Eolian/ Stream Processes | Fluvial Erosion and Deposition | 0 to 15 | no influence | moderately coarse | 10-20 |
| 468 | Canyons | Metavolcanic, Metasedimentary, Serpentine | Tectonic Folding/Uplift/Erosion/ Eolian | Fluvial, Mass Wasting, and Colluvial Erosion | 60 to 90 | mixed | medium | 0-2 |
| 518 | Canyons | Basalt | Lava Flow/Uplift/Erosion | Fluvial, Mass Wasting, and Colluvial Erosion | 60 to 90 | n/a | n/a | 0-1 |
| 532 | Trough Walls, Cirques, & Alpine Ridges | Undifferentiated | Glaciation/Glacial-Periglacial Erosion | Fluvial, Mass Wasting, and Colluvial Erosion | 10 to 90 | n/a | n/a | 0-1 |
| 558 | Canyons | Rhyolitic tuff, Granite, Gneiss/Schist. | PyroclasticFlows and IgneousIntrusives/Uplift/ Erosion | Fluvial, Mass Wasting, and Colluvial Erosion | 60 to 90 | n/a | n/a | 0-1 |
| 567 | Mountain Slopes, Steep | Metavolcanic, Metasedimentary, Serpentine | Tectonic Folding/Uplift/Erosion | Fluvial, Mass Wasting, and Colluvial Erosion | 30 to 60 | n/a | n/a | 0-1 |
| 568 | Canyons | Metavolcanic, Metasedimentary, Serpentine | Tectonic Folding/Uplift/ Erosion | Fluvial, Mass Wasting, and Colluvial Erosion | 60 to 90 | n/a | n/a | 0-1 |
| 600 | WATER |  |  |  |  |  |  |  |
| 736 | Basins, Fans, and Terraces | Undifferentiated | Undifferentiated/Eolian/ Fluvial-MassWasting | Mass Wasting/Fluvial Erosion and Deposition | 15 to 50 | no influence | moderately coarse to fine | 10-20 |
| 832 | Alpine Ridges | Undifferentiated | Glaciation/Glacial-Periglacial Erosion/Eolian | Mass Wasting and Colluvial Erosion | 60 to 90 | thick and mixed | moderately coarse to medium | <1-3 |

Soil Classification and Properties

Table 8 contains representative soils and their properties for each Landtype Association.  Listed below is a description of the information contained in each column.

Soil Classification Series Name:  This column lists soil series selected to represent soil characteristics of major extent in each Landtype Association. These soil series or soils with similar characteristics will represent two thirds or more of the area in most polygons of a Landtype Association.  Soils or miscellaneous areas (e.g. rock outcrop) with contrasting characteristics, but of minor extent also occur in most map units.  These are sometimes listed when known.  The soil series list was developed from the National Cooperative Soil Survey (NCSS)/ Terrestrial Ecological Unit Inventory of the Blue Mountain National Forests (USDA Forest Service, in progress) for the Wallowa-Whitman, Umatilla, Malheur and Ochoco National Forests and the NCSS Baker County Soil Survey (USDA NRCS 1997).  For more detailed information about soils distribution, refer to the Terrestrial Ecological Unit Inventory or Landtype inventory (TEUI).  Several soils have yet to be classified to the series and are listed as undetermined.

Soil Taxonomic Subgroup and Great Group:  These columns list the taxonomic subgroup and great group classification of the soils listed.  Taxa are classified according to Keys To Soil Taxonomy, tenth edition (USDA Soil Survey Staff 2006).  The presence, depth and disturbance of volcanic ash from historic volcanic eruptions are usually indicated by the taxa classification.  Soil climate, thin soil mantles, and degree of soil development are also factors indicated by the taxa classification.  For those who make the effort to learn this classification, it is a useful means of understanding basic differences in soil properties.

Soil Extent:  This column contains an estimated proportionate extent of each representative soil.  This percentage is a representation of the modal concept of soil occurrence within a Landtype Association.  Proportionate extent of each soil will vary in different delineations of a map unit.  The extent of a soil series and similar soils will be within twenty percent of the estimate, in most delineations; considered standard for LTA scale and intensity.

Volcanic Ash :  This column lists five classes of volcanic ash mantle: thick mantle, thin mantle, mixed ash, minor ash, and no ash.  Deposition and erosion processes have created a mosaic of undisturbed ash, ash redistributed and mixed with other colluvial or eolian materials, soil materials with only a minor influence of ash and materials devoid of volcanic ash.  Distribution of volcanic ash serves as an index to erosion, deposition, fire frequency, cover by vegetation and litter, and general landscape stability.  Thicker layers indicate more stable or depositional environments while thinner layers indicate erosional environments and possibly higher fire frequency.  And, generally, distribution, depth, and purity are correlated with steepness of slope, slope position, and slope aspect.  The greater purity and depths occur on north aspects and mid to higher elevation gentle slopes and support moist forest.  Infrequently, great depths of volcanic ash can occur along toeslopes where either colluvial or alluvial processes have moved the ash after its initial deposit.  Mounds of wind distributed volcanic ash occur frequently on backslopes of plateaus and less so on summits of plateaus.  Mixed ash occurs on colluvial foot slopes, climatic zones with more frequent fire and areas that receive significant loess deposition.  Soil materials in flood plains and low terraces on valley floors are devoid of ash having been washed away in swift runoff.

The following classes define the amount or influence of volcanic ash for each soil.

Ash mantles (>60 percent volcanic ash; >7 inches thick)

Thick (> 14 inches thick)

Thin (7-14 inches thick)

Mixed ash (30-60 percent volcanic ash; >7 inches thick)

Minor ash influence (5-30 percent volcanic ash; > 7 inches thick)

No ash influence (0-5 percent volcanic ash)

Surface Texture:  For the purpose of this interpretation, “surface” is the layer that commonly supports the root zone for fine and medium size roots.  This column contains the Soil Textural Classes defined in the USDA Soil Survey Manual (USDA Soil Survey 1993), not to be confused with the particle-size class defined in Soil Taxonomy (USDA Soil Survey 1998).  These textural classes are defined below.

Regolith Texture:  Regolith texture is of the unconsolidated material from the base of the surface layer to a bedrock contact. Soils with an ash or loess mantle commonly have a different surface texture than in the material buried beneath the ash.  Textures are grouped using the Soil Textural Classes defined in the USDA Soil Survey Manual (USDA Soil Survey 1993).

Soil Textural Classes are as follows:

coarse -  sands and loamy sands

moderately coarse - sandy loams

medium - very fine sands, loams, silt loams, and silt

moderately fine - clay loams, sandy clay loams, and silty clay loams

fine-  sandy clay, silty clay, and clay

Regolith Rock Fragments (Size and Percent Volume):  This column contains the dominant shape and size of rock fragments as defined in the USDA Soil Survey Manual (USDA Soil Survey Staff 1993).  Gravelly represents angular and spherical rock 2-75 mm diameter.  Cobbly represents angular and spherical rock 75-250 mm.  Stony represents angular and spherical rock greater than 250mm diameter.  The amount of rock fragments is quite variable and ranges are given to indicate this variability and the general trend.

Depth to Bedrock:  This column contains the depth of unconsolidated soil or surficial deposits to consolidated bedrock.  This interpretation was based upon TEUI soil series descriptions and observations of representative soils in the field.

Parent Material:  This column contains the dominant bedrock or type of surficial deposit influencing regolith properties.

Soil Climate:  This column contains general soil temperature and moisture regimes.  These regimes are based upon soil taxa and plant association groups.

Table 8.  Soil Classification and Properties

| MUS | Soil Series Name | Subgroup | Great Group | Soil Extent | Volcanic Ash | Surface Texture | Regolith Texture | Regolith Rock Fragments (size/%volume) | Depth to Bedrock | Parent Material | Soil Climate |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |
| 114 | Mountemily | Typic | Vitricryands | 50 | thick | medium | medium | cobbly 35 - 75 | >10 | basalt | Cold, Moist |
|  | Limberjim | Alfic | Udivitrands | 30 | thick | medium | medium | cobbly 35 - 65 | 3-5 | basalt | Cold, Moist |
| 115 | Mountemily | Typic | Vitricryands | 50 | thick | medium | medium | cobbly 35 - 75 | 10-20 | basalt | Cold, Moist |
|  | Limberjim | Alfic | Udivitrands | 30 | thick | medium | medium | cobbly 35 - 65 | 3-5 | basalt | Cold, Moist |
| 116 | Limberjim | Alfic | Udivitrands | 30 | thick | medium | medium | cobbly 35 - 65 | 3-5 | basalt | Cold, Moist |
|  | Syrupcreek | Alfic | Udivitrands | 25 | thick | medium | medium | cobbly 35 - 65 | 2-3 | basalt | Cold, Moist |
|  | Mountemily | Typic | Vitricryands | 15 | thick | medium | medium | cobbly 35 - 75 | 10-20 | basalt | Cold, Moist |
|  | Troutmeadows | Typic | Vitricryands | 10 | thick | medium | moderately coarse | stony 40 - 75 | 2-3 | basalt | Cold, Moist |
| 117 | Limberjim | Alfic | Udivitrands | 30 | thick | medium | medium | cobbly 35 - 65 | 3-5 | basalt | Cold, Moist |
|  | Mountemily | Typic | Vitricryands | 20 | thick | medium | medium | cobbly 35 - 75 | >8 | basalt | Cold, Moist |
|  | Bennettcreek | Vitrandic | Haploxeralfs | 15 | mixed | medium | medium | gravelly 35 - 65 | 2-3 | basalt | Cool, Somewhat dry |
|  | Rebarrow | Alfic | Udivitrands | 10 | thick | medium | medium | stony 35 - 65 | >8 | basalt | Cold, Moist |
|  | Syrupcreek | Alfic | Udivitrands | 5 | thick | medium | medium | cobbly 35 - 65 | 2-3 | basalt | Cold, Moist |
| 118 | Harl | Typic | Udivitrands | 30 | thick | medium | medium | gravelly 35 - 65 | >8 | basalt | Cold, Moist |
|  | Limberjim | Alfic | Udivitrands | 25 | thick | medium | medium | cobbly 35 - 65 | 3-5 | basalt | Cool, Moist |
|  | Larabee | Vitrandic | Argixerolls | 15 | mixed | medium | moderately fine | cobbly 35 - 65 | 2-3 | basalt | Cool, Dry |
|  | Bocker | Lithic | Haploxerolls | 10 | minor | medium | medium | gravelly 35 - 65 | <1 | basalt | Cool, Dry |
| 124 | Geisercreek | Alfic | Udivitrands | 30 | thick | medium | moderately fine | <35 | >10 | volcaniclastic deposits | Cool, Moist |
|  | Btree | Alfic | Udivitrands | 25 | thick | medium | fine | cobbly 35 - 65 | 3-5 | volcaniclastic deposits | Cool, Moist |
|  | Ingrampoint | Alfic | Udivitrands | 15 | thick | medium | fine | cobbly 35 - 65 | 2-3 | volcaniclastic deposits | Cool, Moist |
|  | Olot, anss | Typic | Vitrixerands | 10 | thick | medium | moderately coarse | cobbly 35 - 65 | 2-3 | volcaniclastic deposits | Cool, Somewhat dry |
| 125 | Geisercreek | Alfic | Udivitrands | 40 | thick | medium | moderately fine | <35 | 10-20 | volcaniclastic deposits | Cool, Moist |
|  | Btree | Alfic | Udivitrands | 25 | thick | medium | fine | cobbly 35 - 65 | 3-5 | volcaniclastic deposits | Cool, Moist |
|  | Ingrampoint | Alfic | Udivitrands | 15 | thick | medium | fine | cobbly 35 - 65 | 2-3 | volcaniclastic deposits | Cool, Moist |
| 126 | Geisercreek | Alfic | Udivitrands | 40 | thick | medium | moderately fine | <35 | 10-20 | volcaniclastic deposits | Cool, Moist |
|  | Btree | Alfic | Udivitrands | 25 | thick | medium | fine | cobbly 35 - 65 | 3-5 | volcaniclastic deposits | Cool, Moist |
|  | Ingrampoint | Alfic | Udivitrands | 15 | thick | medium | fine | cobbly 35 - 65 | 2-3 | volcaniclastic deposits | Cool, Moist |
| 127 | Ingrampoint | Alfic | Udivitrands | 40 | thick | medium | fine | cobbly 35 - 65 | 2-3 | volcaniclastic deposits | Cool, Moist |
|  | Btree | Alfic | Udivitrands | 25 | thick | medium | fine | cobbly 35 - 65 | 3-5 | volcaniclastic deposits | Cool, Moist |
|  | Lick | Alfic | Hapludalfs | 15 | thick | medium | moderately fine | gravelly 35 - 65 | 3-5 | volcaniclastic deposits | Cool, Moist |
| 131 | Bucketlake | Typic | Vitricryands | 30 | thick | medium | moderately coarse | gravelly 35 - 65 | 10-20 | glacial - undifferentiated | Cool, Moist |
|  | Bulgar | Typic | Udivitrands | 20 | thick | medium | moderately coarse | cobbly 35 - 65 | 10-20 | glacial - undifferentiated | Cool, Moist |
|  | Mudlakebasin | Typic | Vitricryands | 15 | thick | medium | moderately coarse | gravelly 35 - 65 | 2-3 | glacial - undifferentiated | Cool, Moist |
| 131 (cont) | Ducklake | Typic | Vitricryands | 10 | thick | medium | moderately coarse | cobbly 35 - 65 | 3-5 | glacial - undifferentiated | Cool, Moist |
|  | Tyeecreek | Alfic | Vitricryands | 5 | thick | medium | moderately fine | gravelly 35 - 65 | 10-20 | glacial - undifferentiated | Cool, Moist |
| 132 | Mudlakebasin | Typic | Vitricryands | 50 | thick | medium | moderately coarse | gravelly 35 - 65 | 2-3 | glacial - undifferentiated | Cold, Moist |
|  | Rock outcrop |  |  | 30 |  |  |  |  | 0 | glacial - undifferentiated |  |
| 133 | Verdeplane | Pachic | Hapludolls | 30 | none | medium | moderately coarse | cobbly 15- 85 | >20 | Alluvium | Cool, Moist |
|  | Digit | Typic | Vitricryands | 25 | thick | medium | moderately fine | <35 | >20 | Alluvium | Cold, Moist |
|  | Bullroar | Typic | Udivitrands | 15 | thick | medium | moderately coarse | cobbly 35 - 65 | >20 | Alluvium | Cool, Moist |
|  | Bigbouldercreek | Typic | Udivitrands | 10 | thick | medium | medium | <35 | >20 | Alluvium | Cool, Moist |
| 135 | Digit | Typic | Vitricryands | 40 | thick | medium | moderately fine | <35 | 10-20 | Ashy colluvium | Cold, Moist |
|  | Bodale | Pachic | Haplocryolls | 25 | none | medium | moderately coarse | gravelly 15 - 75 | 10-20 | Ashy colluvium | Cold, Wet |
|  | Bandarrow | Typic | Cryaquolls | 15 | none | medium | medium | <15 | 10-20 | Ashy colluvium | Cold, Wet |
| 144 | Geisercreek | Alfic | Udivitrands | 40 | thick | medium | moderately fine | <35 | >10 | lacustrine deposition and burial by volcanic flows | Cool, Moist |
|  | Btree | Alfic | Udivitrands | 25 | thick | medium | fine | cobbly 35 - 65 | 3-5 | lacustrine deposition and burial by volcanic flows | Cool, Moist |
|  | Lick | Alfic | Hapludalfs | 15 | thin | medium | moderately fine | gravelly 35 - 65 | 3-5 | lacustrine deposition and burial by volcanic flows | Cool, Moist |
| 146 | Geisercreek | Alfic | Udivitrands | 40 | thick | medium | moderately fine | <35 | >20 | lacustrine deposition and burial by volcanic flows | Cool, Moist |
|  | Limberjim | Alfic | Udivitrands | 25 | thick | medium | medium | cobbly 35 - 65 | 3-5 | lacustrine deposition and burial by volcanic flows | Cool, Moist |
|  | Btree | Alfic | Udivitrands | 15 | thick | medium | fine | cobbly 35 - 65 | 3-5 | lacustrine deposition and burial by volcanic flows | Cool, Moist |
| 155 | Towermountain | Typic | Vitricryands | 40 | thick | medium | medium | cobbly 35 - 65 | 2-3 | pyroclastic flows | Cold, Moist |
|  | Gutridge, rtss | Typic | Udivitrands | 25 | thick | medium | medium | gravelly 35 - 65 | 3-5 | pyroclastic flows | Cool, Moist |
|  | Kingbolt, rtss | Typic | Vitrixerands | 15 | thick | medium | medium | gravelly 35 - 65 | 2-3 | pyroclastic flows | Cool, Somewhat dry |
| 156 | Stalter, deep | Typic | Udivitrands | 30 | thick | medium | moderately coarse | gravelly 35 - 65 | 3-5 | granodiorite | Cool, Moist |
|  | Hoffer | Typic | Vitricryands | 20 | thick | medium | moderately coarse | <15 | 3-7 | granodiorite | Cold, Moist |
|  | Stalter | Typic | Udivitrands | 15 | thick | medium | moderately coarse | gravelly 35 - 65 | 2-3 | granodiorite | Cool, Moist |
|  | McCalpine-meadow | Typic | Vitricryands | 10 | thick | medium | moderately coarse | stony 40 - 75 | 2-3 | granodiorite | Cold, Moist |
|  | Angelpeak, rtss | Typic | Vitricryands | 5 | thick | medium | moderately coarse | gravelly 35 - 65 | 3-5 | granodiorite | Very Cold, Moist |
| 157 | Ufish | Typic | Vitricryands | 30 | thick | medium | moderately coarse | stony 35 - 65 | 3-5 | granodiorite | Cold, Moist |
|  | Fourthcreek | Typic | Vitrixerands | 25 | thick | medium | moderately coarse | <35 | 2-3 | granodiorite | Cool, Somewhat dry |
|  | McCalpine-meadow | Typic | Vitricryands | 15 | thick | medium | moderately coarse | stony 40 - 75 | 2-3 | granodiorite | Cold, Moist |
|  | Reedmine | Typic | Udivitrands | 10 | thick | medium | moderately coarse | gravelly 35 - 65 | 3-5 | granodiorite | Cool, moist |
| 158 | McCalpine-meadow | Typic | Vitricryands | 30 | thick | medium | moderately coarse | stony 40 - 75 | 2-3 | granodiorite | Cold, Moist |
|  | Prouty | Andic | Dystrocryepts | 25 | mixed | medium | moderately coarse | gravelly 35 - 65 | 2-3 | granodiorite | Cold, Moist |
|  | Rockcreekbutte | Haplo-xerandic | Humicryepts | 15 | minor | coarse | coarse | stony 35 - 65 | 2-3 | granodiorite | Very Cold, Moist |
|  | Ufish | Typic | Vitricryands | 10 | thick | medium | moderately coarse | stony 35 - 65 | 3-5 | granodiorite | Cold, Moist |
| 165 | Towermountain, mvss | Typic | Vitricryands | 30 | thick | medium | medium | cobbly 35 - 65 | 2-3 | metavolcanic and metasedimentary rocks | Cold, Moist |
|  | Marblepoint, mvss | Andic | Haplocryepts | 25 | thin | medium | medium | cobbly 35 - 65 | 10-20 | metavolcanic and metasedimentary rocks | Cold, Moist |
|  | Angelpeak | Typic | Vitricryands | 15 | thick | medium | moderately coarse | gravelly 35 - 65 | 3-5 | metavolcanic and metasedimentary rocks | Cold, Moist |
|  | Bordengulch | Andic | Haplocryepts | 10 | thin | medium | moderately coarse | gravelly 35 - 65 | 2-3 | metavolcanic and metasedimentary rocks | Cold, Moist |
| 166 | Bordengulch | Andic | Haplocryepts | 40 | thin | medium | moderately coarse | gravelly 35 - 65 | 2-3 | metavolcanic and metasedimentary rocks | Cold, Moist |
|  | Threecent | Typic | Udivitrands | 25 | thick | medium | medium | gravelly 40 - 70 | 2-3 | metavolcanic and metasedimentary rocks | Cool, Moist |
| - | Analulu | Vitrandic | Haploxerepts | 15 | thin | medium | medium | gravelly 35 - 65 | 2-3 | metavolcanic and metasedimentary rocks | Cool, Somewhat dry |
| 167 | Honeymooncan | Alfic | Udivitrands | 25 | thick | medium | moderately fine | gravelly 35 - 65 | 3-5 | metavolcanic and metasedimentary rocks | Cool, Moist |
|  | Twobit | Typic | Udivitrands | 15 | thick | medium | medium | cobbly 35 - 65 | 2-3 | metavolcanic and metasedimentary rocks | Cool, Moist |
| 167 (cont) | Pasturecreek | Andic | Eutrudepts | 10 | mixed | medium | moderately coarse | gravelly 35 - 80 | >8 | metavolcanic and metasedimentary rocks | Cool, Moist |
| 168 | Pasturecreek | Andic | Eutrudepts | 30 | mixed | medium | moderately coarse | gravelly 35 - 80 | >8 | metavolcanic and metasedimentary rocks | Cool, Moist |
|  | Gutridge | Typic | Udivitrands | 25 | thick | medium | medium | gravelly 35 - 75 | 3-5 | metavolcanic and metasedimentary rocks | Cool, Moist |
|  | Twobit | Typic | Udivitrands | 15 | thick | medium | medium | cobbly 35 - 65 | 2-3 | metavolcanic and metasedimentary rocks | Cool, Moist |
|  | Honeymooncan | Alfic | Udivitrands | 10 | thick | medium | moderately fine | gravelly 35 - 65 | 3-5 | metavolcanic and metasedimentary rocks | Cool, Moist |
| 176 | undetermined1* | Typic | Haploxerepts | 30 | minor | medium | medium | gravelly/ cobbly 30-50 | 1-2 | metavolcanic and metasedimentary rocks | Cool, Dry |
|  | undetermined2* | Vitrandic | Haploxerepts | 25 | mixed | medium | moderately fine | gravelly/ cobbly 30-50 | 1.5-3 | metavolcanic and metasedimentary rocks | Cool, Dry |
|  | undetermined3* | Lithic | Haploxerepts | 30 | minor | medium | medium | gravelly/ cobbly 45-70 | <1 | metavolcanic and metasedimentary rocks | Cool, Dry |
| 177 | undetermined4* | Typic | Udivitrands (Vitrandepts) | 40 | thick | medium | moderately fine | gravelly/ cobbly 30-50 | 2-3 | metavolcanic and metasedimentary rocks | Cool, Moist |
|  | undetermined3* | Lithic | Haploxerepts | 25 | minor | medium | medium | gravelly/ cobbly 45-70 | <1 | metavolcanic and metasedimentary rocks | Cool, Dry |
|  | undetermined5* | Typic | Vitricryands | 15 | thick | medium | medium | gravelly/ cobbly 45-70 | 2-3 | metavolcanic and metasedimentary rocks | Cold, Moist |
| 214 | Fourcorner, bss | Vertic | Palexerolls | 50 | minor | fine | fine | <15 | 3-5 | basalt | Cool, Dry |
|  | Cougarrock, bss | Vitrandic | Haploxeralfs | 30 | mixed | medium | moderately fine | gravelly 35 - 65 | 2-3 | basalt | Cool, Somewhat dry |
| 215 | Klicker | Vitrandic | Argixerolls | 50 | minor | medium | moderately fine | gravelly 35 - 65 | 2-3 | basalt | Cool, Dry |
|  | Larabee | Vitrandic | Argixerolls | 30 | mixed | medium | moderately fine | cobbly 35 - 65 | 2-3 | basalt | Cool, Dry |
| 216 | Larabee | Vitrandic | Argixerolls | 40 | mixed | medium | moderately fine | cobbly 35 - 65 | 2-3 | basalt | Cool, Dry |
|  | Bennettcreek | Vitrandic | Haploxeralfs | 25 | mixed | medium | medium | gravelly 35 - 65 | 2-3 | basalt | Cool, Dry |
|  | Wonder | Vitrandic | Haploxerepts | 15 | thin | medium | medium | stony 35 - 65 | 2-3 | basalt | Cool, Somewhat dry |
| 217 | Klickson | Vitrandic | Argixerolls | 40 | mixed | medium | moderately fine | cobbly 35 - 80 | 3-5 | basalt | Cool, Dry |
|  | Larabee | Vitrandic | Argixerolls | 25 | mixed | medium | moderately fine | cobbly 35 - 65 | 2-3 | basalt | Cool, Dry |
|  | Bigcow | Vitrandic | Haploxerepts | 15 | thin | medium | medium | gravelly 35 - 65 | 3-7 | basalt | Cool, Somewhat dry |
| 218 | Klicker | Vitrandic | Argixerolls | 30 | minor | medium | moderately fine | gravelly 35 - 65 | 2-3 | basalt | Cool, Dry |
|  | Fivebit | Lithic Ultic | Haploxerolls | 20 | minor | medium | medium | gravelly 35 - 70 | 0.8-2 | basalt | Cool, Dry |
|  | Klickson | Vitrandic | Argixerolls | 15 | mixed | medium | moderately fine | cobbly 35 - 80 | 3-5 | basalt | Cool, Dry |
|  | Anatone | Lithic | Haploxerolls | 10 | minor | medium | medium | gravelly 35 - 85 | 0.8-2 | basalt | Cool, Dry |
|  | Larabee | Vitrandic | Argixerolls | 5 | mixed | medium | moderately fine | cobbly 35 - 65 | 2-3 | basalt | Cool, Dry |
| 224 | Cleymor | Vertic | Argixerolls | 40 | minor | moderately fine | fine | <15 | >10 | metavolcanic and metasedimentary rocks | Cool, Dry |
|  | Unity | Vertic | Palexeralfs | 25 | thin | medium | fine | <15 | >10 | metavolcanic and metasedimentary rocks | Cool, Dry |
| 224 (cont) | Oxbone | Vitrandic | Haploxeralfs | 15 | mixed | medium | moderately fine | <15 | 3-5 | metavolcanic and metasedimentary rocks | Cool, Somewhat dry |
| 226 | Cotay | Vitrandic | Haploxeralfs | 30 | mixed | medium | moderately fine | cobbly 35 - 80 | 2-3 | metavolcanic and metasedimentary rocks | Cool, Somewhat dry |
|  | Oxbone | Vitrandic | Haploxeralfs | 20 | mixed | medium | moderately fine | <15 | 3-5 | metavolcanic and metasedimentary rocks | Cool, Somewhat dry |
|  | Cougarrock | Vitrandic | Haploxeralfs | 15 | mixed | medium | moderately fine | gravelly 35 - 70 | 2-3 | metavolcanic and metasedimentary rocks | Cool, Somewhat dry |
|  | Humarel | Vitrandic | Argixerolls | 10 | minor | mod-erately fine | fine | gravelly 35 - 65 | 2-3 | metavolcanic and metasedimentary rocks | Cool, Somewhat dry |
|  | Kingbolt | Typic | Vitrixerands | 5 | thick | medium | medium | gravelly 35 - 65 | 2-3 | metavolcanic and metasedimentary rocks | Cool, Somewhat dry |
| 227 | Cougarrock | Vitrandic | Haploxeralfs | 50 | mixed | medium | moderately fine | gravelly 35 - 70 | 2-3 | volcaniclastic deposits | Cool, Somewhat dry |
|  | Humarel | Vitrandic | Argixerolls | 30 | minor | moderately fine | fine | gravelly 35 - 65 | 2-3 | volcaniclastic deposits | Cool, Somewhat dry |
| 231 | Bigelk | Vitrandic | Haploxerolls | 30 | minor | moderately coarse | moderately coarse | stony 35 - 65 | 10-20 | glacial - undifferentiated | Cool, Somewhat dry |
|  | Lakefork | Typic | Udivitrands | 25 | thick | medium | medium | stony 45 - 80 | 10-20 | glacial - undifferentiated | Cool, Moist |
|  | Warfield | Vitrandic | Haploxerepts | 15 | mixed | moderately coarse | moderately coarse | stony 50 - 80 | 3-5 | glacial - undifferentiated | Cool, Somewhat dry |
|  | Twocolor | Typic | Vitrixerands | 10 | thick | medium | moderately coarse | stony 35 - 65 | 10-20 | glacial - undifferentiated | Cool, Somewhat dry |
| 232 | Lakefork | Typic | Udivitrands | 40 | thick | medium | moderately coarse | stony 45 - 80 | >8 | glacial - undifferentiated | Cool, Moist |
|  | Rock outcrop |  |  | 25 |  |  |  |  | 0 | glacial - undifferentiated |  |
| 232 (cont) | Moodybasin | Vitrixerandic | Humicryepts | 15 | minor | moderately coarse | moderately coarse | stony 55 - 75 | 2-3 | glacial - undifferentiated | Very Cold, Moist |
| 233 | Stevenscreek | Vitrandic | Haploxeralfs | 40 | minor | moderately fine | moderately fine | cobbly 45 – 60 | >20 | allluvium | Cool, Dry |
|  | Ranes | Vitrandic | Haploxeralfs | 40 | thin | medium | medium | cobbly 35 - 65 | >20 | alluvium | Cool, Dry |
| 235 | Langrell | Pachic | Haploxerolls | 50 | none | medium | medium | gravelly 35 - 65 | >8 | colluvium/ alluvium | Cool, Dry |
|  | Stevenscreek | Vitrandic | Haploxeralfs | 30 | minor | moderately fine | moderately fine | cobbly 45 - 60 | >8 | colluvium/ alluvium | Cool, Dry |
| 236 | Stevenscreek | Vitrandic | Haploxeralfs | 50 | minor | moderately fine | moderately fine | cobbly 45 - 60 | >20 | alluvium | Cool, Dry |
|  | Ranes | Vitrandic | Haploxeralfs | 30 | thin | medium | medium | cobbly 35 - 65 | >20 | alluvium | Cool, Dry |
| 244 | Volstead | Vitrandic | Argixerolls | 40 | mixed | medium | moderately fine | <15 | 3-5 | lacustrine deposition with volcanic burial | Cool, Dry |
|  | Quirk | Vitrandic | Palexerolls | 25 | mixed | medium | fine | <35 | 2-3 | lacustrine deposition with volcanic burial | Cool, Dry |
|  | Tamarackcanyon | Vitrandic | Haploxeralfs | 15 | mixed | moderately fine | fine | cobbly 35 - 65 | 2-3 | lacustrine deposition with volcanic burial | Cool, Dry |
| 246 | Quirk | Vitrandic | Palexerolls | 50 | mixed | medium | fine | <35 | 2-3 | lacustrine deposition and burial by volcanic flows | Cool, Dry |
|  | Klicker | Vitrandic | Argixerolls | 30 | minor | medium | moderately fine | gravelly 35 - 65 | 2-3 | lacustrine deposition and burial by volcanic flows | Cool, Dry |
| 256 | Kingbolt, rtss | Typic | Vitrixerands | 50 | thick | medium | medium | gravelly 35 - 65 | 2-3 | pyroclastic flows | Cool, Somewhat dry |
| 256 (cont) | Eastpine, rtss | Vitrandic Ultic | Haploxerolls | 30 | mixed | medium | medium | cobbly 35 - 65 | 2-3 | pyroclastic flows | Cool, Somewhat dry |
| 257 | McWillar | Alfic | Vitrixerands | 40 | thick | medium | moderately fine | gravelly 35 - 65 | 3-5 | pyroclastic flows | Cool, Somewhat dry |
|  | Analulu, rtss | Vitrandic | Haploxerepts | 25 | minor | moderately coarse | medium | gravelly 35 - 65 | 2-3 | pyroclastic flows | Cool, Dry |
|  | Threecabin, rtss | Vitrandic | Haploxerepts | 15 | minor | medium | medium | gravelly 35 - 65 | 3-5 | pyroclastic flows | Cool, Somewhat dry |
| 258 | Threecabin, rtss | Vitrandic | Haploxerepts | 50 | minor | medium | medium | gravelly 35 - 65 | 3-5 | pyroclastic flows | Cool, Somewhat dry |
|  | Analulu, rtss | Vitrandic | Haploxerepts | 30 | minor | moderately coarse | medium | gravelly 35 - 65 | 2-3 | pyroclastic flows | Cool, Dry |
| 265 | Hondu, mvss | Vitrandic | Haploxerepts | 50 | thin | medium | moderately coarse | gravelly 35 - 65 | 10-20 | metavolcanic and metasedimentary rocks | Cool, Somewhat dry |
|  | Deck | Vitrandic | Haploxerolls | 30 | minor | medium | moderately coarse | cobbly 35 - 65 | 2-3 | metavolcanic and metasedimentary rocks | Cool, Somewhat dry |
| 266 | Deck | Vitrandic | Haploxerolls | 50 | mixed | medium | moderately fine | <15 | 2-3 | metavolcanic and metasedimentary rocks | Cool, Dry |
|  | Eastlakes | Lithic | Humicryepts | 30 | minor | medium | medium | gravelly 50 - 70 | 0.8-2 | metavolcanic and metasedimentary rocks | Cold, Dry |
| 267 | Analulu | Vitrandic | Haploxerepts | 40 | thin | medium | medium | gravelly 35 - 65 | 2-3 | metavolcanic and metasedimentary rocks | Cool, Somewhat dry |
|  | Kettlecreek | Vitrandic | Haploxerolls | 25 | mixed | moderately coarse | moderately coarse | gravelly 55 - 85 | 3-5 | metavolcanic and metasedimentary rocks | Cool, Dry |
|  | Payraise | Vitrandic | Haploxeralfs | 15 | thin | medium | moderately coarse | stony 35 - 65 | >8 | metavolcanic and metasedimentary rocks | Cool, Somewhat dry |
| 268 | Analulu | Vitrandic | Haploxerepts | 40 | thin | medium | medium | gravelly 35 - 65 | 2-3 | metavolcanic and metasedimentary rocks | Cool, Somewhat dry |
|  | Rock outcrop |  |  | 25 |  |  |  |  | 0 | metavolcanic and metasedimentary rocks |  |
|  | Blackgulch | Lithic Ultic | Haploxerolls | 15 | minor | medium | medium | cobbly 35 - 65 | 0.8-2 | metavolcanic and metasedimentary rocks | Cool, Dry |
| 273 | undetermined2* | Vitrandic | Haploxerepts | 35 | mixed | medium | moderately fine | gravelly/ cobbly 30-50 | 1.5-3 | Alluvium: Sedimentary - graywacke | Cool, Dry |
|  | undetermined6* | Lithic Ultic | Argixerolls | 25 | none | medium | medium | gravelly/ cobbly 20-60 | <1 | Alluvium: Sedimentary - graywacke | Cool, Dry |
|  | undetermined3* | Lithic | Haploxerepts | 20 | minor | medium | medium | gravelly/ cobbly 45-70 | <1 | Alluvium: Sedimentary - graywacke | Cool, Dry |
| 275 | undetermined1 | Typic | Haploxerepts | 60 | minor | medium | medium | gravelly/ cobbly 30-50 | 1-2 | Sedimentary – greywacke, shales | Cool, Dry |
|  | undetermined3* | Lithic | Haploxerepts | 25 | minor | medium | medium | gravelly/ cobbly 45-70 | <1 | Sedimentary – greywacke, shales | Cool, Dry |
| 276 | undetermined1 | Typic | Haploxerepts | 35 | minor | medium | medium | gravelly/ cobbly 30-50 | 1-2 | Sedimentary – greywacke, shales | Cool, Dry |
|  | undetermined3* | Lithic | Haploxerepts | 20 | minor | medium | medium | gravelly/ cobbly 45-70 | <1 | Sedimentary – greywacke, shales | Cool, Dry |
| 277 | undetermined2* | Vitrandic | Haploxerepts | 30 | mixed | medium | moderately fine | gravelly/ cobbly 30-50 | 1.5-3 | Sedimentary – greywacke, shales | Cool, Dry |
|  | undetermined3* | Lithic | Haploxerepts | 20 | minor | medium | medium | gravelly/ cobbly 45-70 | <1 | Sedimentary – greywacke, shales | Cool, Dry |
| 315 | Clearline | Vitrandic | Haploxerolls | 50 | mixed | medium | moderately coarse | cobbly 40 - 75 | 3-5 | Basalt | Cool, Dry |
|  | Imnaha | Vitrandic | Argixerolls | 30 | mixed | medium | medium | gravelly 35 - 75 | 2-3 | Basalt | Cool, Dry |
| 316 | Anatone | Lithic | Haploxerolls | 50 | minor | medium | medium | gravelly 35 - 85 | 0.8-2 | Basalt | Cool, Dry |
|  | Bocker | Lithic | Haploxerolls | 30 | minor | medium | medium | gravelly 35 - 65 | <1 | Basalt | Cool, Dry |
| 317 | Anatone | Lithic | Haploxerolls | 30 | minor | medium | medium | gravelly 35 - 85 | 0.8-2 | Basalt | Cool, Dry |
|  | Imnaha | Vitrandic | Argixerolls | 25 | mixed | medium | medium | gravelly 35 - 75 | 2-3 | Basalt | Cool, Dry |
|  | Rock outcrop |  |  | 15 |  |  |  |  | 0 | Basalt |  |
|  | Bocker | Lithic | Haploxerolls | 10 | minor | medium | medium | gravelly 35 - 65 | <1 | Basalt | Cool, Dry |
| 318 | Anatone | Lithic | Haploxerolls | 30 | minor | medium | medium | gravelly 35 - 85 | 0.8-2 | Basalt | Cool, Dry |
|  | Rock outcrop |  |  | 25 |  |  |  |  | 0 | Basalt |  |
|  | Bocker | Lithic | Haploxerolls | 15 | minor | medium | medium | gravelly 35 - 65 | <1 | Basalt | Cool, Dry |
|  | Imnaha | Vitrandic | Argixerolls | 10 | mixed | medium | medium | gravelly 35 - 75 | 2-3 | Basalt | Cool, Dry |
| 326 | Roostercomb | Typic | Argixerolls | 50 | minor | moderately fine | fine | cobbly 35 - 65 | 2-3 | volcaniclastic deposits | Cool, Dry |
|  | Ateron | Lithic | Argixerolls | 30 | minor | medium | fine | cobbly 35 – 65 | 0.8-2 | volcaniclastic deposits | Cool, Dry |
| 327 | Hafmau | Lithic Ultic | Argixerolls | 50 | minor | moderately coarse | fine | cobbly 35 - 85 | 0.8-2 | volcaniclastic deposits | Cool, Dry |
|  | Harlow | Lithic | Argixerolls | 30 | minor | medium | fine | cobbly 35 - 65 | 0.8-2 | volcaniclastic deposits | Cool, Dry |
| 332 | Rock outcrop |  |  | 40 |  |  |  |  | 0 | glacial - undifferentiated |  |
|  | Moodybasin | Vitrixerandic | Humicryepts | 25 | minor | moderately coarse | moderately coarse | stony 55 - 75 | 2-3 | glacial - undifferentiated | Cold, Dry |
|  | Muddycreek | Andic | Humicryepts | 15 | minor | coarse | coarse | stony 35 - 80 | >8 | glacial - undifferentiated | Cold, Moist |
| 333 | Phys | Typic | Argixerolls | 40 | minor | medium | moderately fine | cobbly 35 - 65 | >20 | alluvium | Cool, Dry |
|  | Campcreek | Vertic | Palexerolls | 25 | minor | medium | fine | <35 | >20 | alluvium | Cool, Dry |
|  | Lizard | Typic | Palexerolls | 15 | minor | medium | fine | gravelly 35 - 65 | >20 | alluvium | Cool, Dry |
| 356 | Wintercanyon, rtss | Lithic Ultic | Haploxerolls | 40 | minor | medium | medium | gravelly 35 - 75 | 0.8-2 | pyroclastic flows and igneous intrusive with uplift | Cool, Dry |
|  | VanPatten | Lithic | Humicryepts | 25 | minor | moderately coarse | moderately coarse | gravelly 35 - 65 | 0.8-2 | pyroclastic flows and igneous intrusive with uplift | Cool, Dry |
|  | Van Wagoner | Lithic | Haploxerolls | 15 | minor | moderately coarse | moderately coarse | cobbly 35 - 65 | 0.8-2 | pyroclastic flows and igneous intrusive with uplift | Cool, Dry |
| 357 | VanPatten | Lithic | Humicryepts | 50 | minor | moderately coarse | moderately coarse | stony 35 - 65 | 0.8-2 | pyroclastic flows and igneous intrusive with uplift | Cool, Dry |
|  | Van Wagoner | Lithic | Haploxerolls | 30 | minor | moderately coarse | moderately coarse | cobbly 35 - 65 | 0.8-2 | pyroclastic flows and igneous intrusive with uplift | Cool, Dry |
| 358 | Rock outcrop |  |  | 50 |  |  |  |  | 0 | pyroclastic flows and igneous intrusive with uplift |  |
|  | Powderriver | Lithic | Haploxerepts | 30 | minor | moderately coarse | moderately coarse | gravelly 35 - 65 | 0.8-2 | pyroclastic flows and igneous intrusive with uplift | Cool, Dry |
| 365 | Bluecanyon, mvss | Lithic | Haploxerolls | 80 | minor | medium | medium | gravelly 35 - 65 | 0.8-2 | metavolcanic and metasedimentary rocks | Cool, Dry |
| 366 | Bluecanyon | Lithic | Haploxerolls | 50 | minor | medium | medium | gravelly 45 - 75 | 0.8-2 | metavolcanic and metasedimentary rocks | Cool, Dry |
|  | Analulu | Vitrandic | Haploxerepts | 30 | minor | moderately coarse | medium | gravelly 35 - 75 | 2-3 | metavolcanic and metasedimentary rocks | Cool, Dry |
| 367 | Hondu | Vitrandic | Haploxeralfs | 50 | thin | medium | moderately coarse | gravelly 35 - 65 | 3-5 | metavolcanic and metasedimentary rocks | Cool, Somewhat dry |
|  | Mcwillar | Alfic | Vitrixerands | 30 | thick | medium | moderately coarse | gravelly 35 - 65 | 3-5 | metavolcanic and metasedimentary rocks | Cool, Somewhat dry |
| 368 | Blackgulch | Lithic Ultic | Haploxerolls | 80 | minor | medium | medium | cobbly 35 - 65 | 0.8-2 | metavolcanic and metasedimentary rocks | Cool, Dry |
| 376 | undetermined3* | Lithic | Haploxerepts | 70 | minor | medium | medium | gravelly/ cobbly 45-70 | <1 | Sedimentary – greywacke, shales | Cool, Dry |
| 377 | undetermined3* | Lithic | Haploxerepts | 70 | minor | medium | medium | gravelly/ cobbly 45-70 | <1 | Sedimentary – greywacke, shales | Cool, Dry |
| 416 | Albee | Vitrandic | Haploxerolls | 50 | mixed | medium | medium | <35 | 2-3 | Basalt | Cool, Dry |
|  | Needhill | Vitrandic | Argixerolls | 30 | mixed | medium | medium | cobbly 35 – 65 | 3-5 | Basalt | Cool, Dry |
| 418 | Cherrycreek | Vitrandic | Haploxerolls | 50 | mixed | medium | medium | cobbly 35 - 65 | 3-5 | Basalt | Cool, Dry |
|  | Anatone, north | Lithic | Haploxerolls | 30 | minor | medium | medium | gravelly 35 - 65 | 0.8-2 | Basalt | Cool, Dry |
| 432 | Burgerbutte | Lithic | Humicryepts | 50 | minor | medium | medium | gravelly 60 - 75 | 0.8-2 | glacial - undifferentiated | Cold, Moist |
|  | Rock outcrop |  |  | 30 |  |  |  |  | 0 | glacial - undifferentiated |  |
| 433 | Witknee | Aquic | Hapludolls | 80 | none | moderately coarse | moderately coarse | gravelly 25-60 | >20 | alluvium | Cool, Seasonally wet |
| 468 | Analulu | Vitrandic | Haploxerepts | 55 | thin | medium | medium | gravelly 35 - 65 | 2-3 | metavolcanic and metasedimentary rocks |  |
|  | Rock outcrop |  |  | 20 |  |  |  |  |  |  |  |
| 518 | Rock outcrop |  |  | 80 |  |  |  |  | 0 | Basalt |  |
| 532 | Rock outcrop |  |  | 80 |  |  |  |  | 0 | glacial - undifferentiated |  |
| 558 | Rock outcrop |  |  | 80 |  |  |  |  | 0 | pyroclastic flows and igneous intrusive with uplift |  |
| 567 | Rock outcrop |  |  | 80 |  |  |  |  | 0 | metavolcanic and metasedimentary rocks |  |
| 568 | Rock outcrop |  |  | 80 |  |  |  |  | 0 | metavolcanic and metasedimentary rocks |  |
| 600 | WATER |  |  |  |  |  |  |  |  |  |  |
| 736 | Riceton | Pachic Ultic | Haploxerolls | 70 | none | moderately coarse | moderately coarse | <35 | 10-20 | alluvium | Cool, Dry |
|  | Damore | Fluv-aquentic | Haploxerolls | 15 | none | medium | medium | gravelly 35 - 65 | >8 | alluvium | Cool, Wet |
|  | Melloe | Typic | Endaquolls | 15 | none | medium | moderately fine | cobbly 40 - 80 | 10-20 | alluvium | Cool, Wet |
| 832 | Moodybasin | Vitrixerandic | Humicryepts | 30 | minor | moderately coarse | moderately coarse | stony 55 - 75 | 2-3 | alluvium | Cool, Moist |
|  | Rock outcrop |  |  | 25 |  |  |  |  |  | alluvium |  |
|  | Burgerbutte | Lithic | Humicryepts | 20 | minor | medium | medium | gravelly 60 - 75 | 0.8-2 | alluvium | Cold, Moist |

Hydrologic Properties and Responses

Table 9 contains hydrologic properties, features, classifications, and major channel processes for each Landtype Association.  Listed below is a brief description of the information contained in each column of the table.

Surface Runoff:  This column contains the interpretation for relative response time for runoff from snowpack melt or high intensity rainstorms to become concentrated flow in first order streams.  This interpretation is an indication of the ability or inability of Landtype Association to absorb and route surface water.  The site factors used to develop this interpretation include: slope gradient; vegetation cover, soil regolith texture and rock fragment content; amount of exposed bedrock; density and type of first order drainages; amount, form and timing of precipitation, and stream patterns.

SLOW - Landtype Associations can absorb a great deal of surface water and runoff normally is well regulated and does not become concentrated in first order streams.  Landtype Association features limit surface water from being routed quickly to first order stream systems.  First order stream channels do not have evidence of scour or non-vegetated deposition.  Normally these Landtype Associations have not had a history of shallow rapid landslides.  Usually Landtype Associations have a set of the following site features:  low slope gradients <25%, more than 80 percent vegetation cover; deep, coarse textured regolith; very little exposed bedrock; low drainage density of confined or entrenched first order streams; area not normally exposed to rain on snow events or high intensity thunder storms.

MODERATE - Landtype Associations absorb some surface water and runoff is somewhat well regulated but concentrated flows routed into first order drainages from infrequently large storms or snowmelt have the potential for high peak runoff flows.  Landtype Association features are somewhat efficient in routing surface water into first order stream systems.  First order stream channels have some evidence of scour.  Normally these Landtype Associations have had an infrequent history of high peak runoff events that cause road drainage failures or rapid sediment transport.  Usually Landtype Associations have a set of the following site features:  slope gradients between 25 and 45 percent; vegetation cover is 30 to 80 percent; regolith depths that vary from shallow to moderately deep; exposed bedrock is less than 25 percent of the area; moderate drainage density of confined or entrenched first order stream systems; area exposed to infrequent rain on snow events or high intensity summer storms.

FLASHY - Landtype Associations do not absorb a great deal of surface water, runoff is poorly regulated and concentrated flows are routed rapidly into first order drainages.  Landtype Association features are extremely efficient in routing surface water into first order stream systems.  First order stream channels have evidence of scour or non-vegetated deposition.  Normally these Landtype Associations have had a relatively frequent history of shallow rapid landslides or snow avalanche.  Usually Landtype Associations have a set of the following site features:  steep slope gradients (45%+); less than 30 percent vegetation cover; shallow regolith; exposed bedrock exceeds 25 percent of the area; high drainage density of confined or entrenched first order streams; area is exposed to frequent rain on snow events or high intensity summer storms.

Channel Density:  This column rates the average number of channels per lineal mile.  A channel is defined as any fluvial feature whether it has annual flow or not.  Channels may be 0 order in class with ephemeral flow or higher order in class with perennial flow.  The measure is lineal distance perpendicular to the slope gradient (except for stream valleys where both perpendicular and parallel lineal distance is considered to take into account the mainstem and tributaries of a stream valley landform).  This measure is useful in predicting drainage crossings for roads and with other landform features, sediment delivery efficiency.

Low:  1-3 channels per mile

Moderate:  3-6 channels per mile

High:  6 channels per mile

Stream Flow Duration/Amount:  The next two columns describe stream flow duration and amount for mainstem streams.  Duration is noted as either perennial or intermittent and amount is the degree of flow expected during the summer months.  This interpretation was based upon field observations of stream flows, Soil Resource Inventory descriptions, and extrapolation from other areas with similar landtype features.

Aquifer Recharge:  This column describes the potential for near surface ground water storage within each Landtype Association.  This interpretation is an indication of the ability of Landtype Associations to regulate stream flows especially late into the season.  It can also help indicate the Landtype Associations that have shallow aquifers that contribute to stream flow recharge and temperature moderation.  Factors used to develop this interpretation include:  soil regolith depth and texture; landform shape, slope exposures and gradient; geologic fracturing and structure; annual precipitation; and surface drainage configuration.

LOW (L) - Landtype Associations have little storage capacity for near surface ground water.  Shallow aquifers are limited and recharge to stream flow is very low.  Summer stream flows are often intermittent or flows are unusually low in comparison to watershed size.  Low aquifer recharge of summer stream flows may be a factor in elevated stream temperatures.  Surface water is concentrated and routed quickly to stream systems causing elevated spring peaks.  Few seeps and springs are present.  Usually Landtype Associations have a set of the following site features:  very shallow regolith over bedrock; landform shape, slope gradient and drainage systems that route surface and subsurface water rapidly to larger order streams; geologic features (faults, fractures, and folds) route subsurface water into deep aquifers or the lack of these features cause subsurface water to be routed quickly to drainage systems; or areas without potential for water table retention that receive low annual precipitation much of which is in the form of rain.

MODERATE (M) - Landtype Associations have storage capacity for near surface ground water but recharge of the aquifer is highly variable which influences recharge to stream flow.  Summer stream flows are usually perennial or intermittent but stream flows are variable.  Aquifer recharge may not be enough to modify summer or winter stream temperatures in all stream systems.  Surface water has the ability to be absorbed and stored for recharge of stream flows but normally not enough to fully charge these shallow aquifers annually.  Seeps and springs are present.  Usually Landtype Associations have a set of the following site features:  soil regolith depth is variable but often moderately deep; landform shape, slope gradient, and drainage systems route surface and subsurface water slowly to larger order streams; geologic features restrict downward movement of groundwater; receive little drainage water from upslope landforms; and areas receive moderate amounts of annual precipitation of which there is an equal amount in the form of rain and snow.

HIGH (H) - Landtype Associations have significant storage capacity for near surface ground water.  Shallow aquifers exist and directly recharge to stream flow.  Summer stream flows are typically perennial and stream flows are high in comparison to other drainage systems.  Aquifer recharge of stream flows may help moderate summer and winter stream temperatures.  Surface water has the ability to be absorbed and stored for recharge of summer stream flows.  Seeps and springs are a common feature.  Usually Landtype Associations have a set of the following site features:  very deep coarse textured regoliths; landform shape, slope gradient, and drainage systems that route surface and subsurface water slowly to larger order streams; geologic features restrict the downward movement of groundwater; receive a tremendous amount of drainage water from upslope landforms; and areas receive high amount of annual precipitation much of which is in the form of snow.

Stream Types:  This column contains the dominant stream types based upon a classification system documented in Rosgen (1994).  Rosgen’s classification provides a morphological description of the channel using stream gradient, width:depth ratio, substrate size, channel confinement, and near channel landform stability.  This classification is useful in broad assessments, monitoring condition, and in setting stream restoration objectives.  Each Landtype Association was evaluated to determine the predominant morphologic type based upon field observations and empirically using aerial photography.

Aa Stream Types- Streams that have extremely steep gradients and are deeply entrenched.  They are most often associated with stream segments in the upper elevation zones of high relief landforms formed from glacial erosion and over-steepening.  Most common channel morphology is debris chutes, vertical steps, with shallow scour pools, and waterfalls. Most common stream reach types are bedrock and colluvial.

A Stream Types - Streams that have steep gradients and are normally entrenched.  Most often associated with stream segments in the mid to upper elevation zones of high relief landforms formed from glacial or fluvial erosional processes.  Most common stream reach type is cascade and step pool.

B Stream Types - Streams that have moderate gradients and entrenchment.  Most often associated with stream segments in the mid elevation zones of high relief landforms formed from glacial or fluvial erosional processes.  Most common stream reach type is step pool and forced step pool.

C Stream Types - Streams that have low gradients and are unconfined from valley walls.  Width depth ratios are high.  These are alluvial channels with broad well defined flood plains.  Most often associated with stream segments in the lower elevation zones of low relief landforms formed from glacial or fluvial depositional processes.  Most common stream reach type is pool riffle channels.

D Stream Types - Streams that have braided channels associated with high bedload deposition.  Most often associated with stream segments in lower elevation zones of low relief landforms formed from glacial or fluvial deposition (outwash).  Most common stream reach type is braided channels.

E Stream Types - Streams that have low gradients and are unconfined from valley walls.  Streams are highly sinuous with finer textured banks and little channel roughness.  Width depth ratios are low.  Most often associated with stream segments in the lower elevation zones of low relief landforms formed from glacial or fluvial depositional processes.  Most common stream reach type is plane bed channels.

F Stream Types - Streams that have low gradients and are entrenched.  Width depth ratios are high.  These are streams that have entrenched meandering channels which are in the process of reestablishing a functional floodplain.  Most often associated with dynamic change of discharge power.  Most common stream reach type is plane bed and pool riffle channels.

G Stream Types - Streams that have moderate to steep gradients and are entrenched.  These streams are usually associated with gullies from erosional events.  Width depth ratios are very low.  Most common stream reach type is plane bed and step pool channels.

Stream Reach Processes:  This column contains the dominant channel processes based upon a classification system documented in Montgomery and Buffington (1993).  This classification system describes stream bed morphology, sediment transport processes, and sediment flux characteristics as controlled by hydraulic discharge and sediment supply.  Channel response is also described based on stream confinement, debris flow impacts, and large woody debris loading and is useful for interpretation of channel response to changes in sediment, wood, and discharge within a stream network.  Channel types for each Landtype Association were identified based upon field experience and aerial photo interpretation and extrapolated using general geomorphic characteristics associated with landtype associations.  The identification of channel types provides a first step for assessing potential channel responses to increases or decreases in discharge and in-channel sediment (Montgomery and Buffington 1993).  According to Montgomery and Buffington:  "The spatial distribution of source, transport, and response reaches governs the distribution of potential impacts and watershed recovery time.  General response for source, transport, and response reaches define patters of sensitivity to altered discharge, sediment supply, or debris flow scour within a watershed".

SOURCE - Source reaches are transport-limited channels that allow for sediment storage.  The most common channel type is colluvial channels.  These channels fill with colluvial deposition from hillslopes, upslope hollows or catchment basins. Increased sediment storage may result in large downslope deliveries of sediment during major channel scouring events.  High discharge may mobilize streambeds, scour streambeds or cause debris flows which transports sediment downstream.  In time, these scoured channels begin to refill with sediment.  This action is intermittent or episodic with various frequencies depending on hydrologic regimes.  In steep, upper elevations, colluvial channels are very active and are not stable enough to store sediment for extended periods of time.

TRANSPORT - Transport reaches are resilient, high gradient channels that are capable of rapidly conveying increased sediment inputs.  The most common channel types are bedrock, cascade, and step pool.

Bedrock channels are confined by exposed bedrock, channel width and channel depth will increase to handle increased discharge.  Moderate changes in discharge or sediment load are rapidly transmitted downstream without significant morphological changes within these reaches.

Cascade channels generally have well armored immobile boulders and are laterally confined by valley walls.  Channel bank cutting or down-cutting are unlikely responses to changes in sediment supply or discharge.  These types of confined channels can also respond to increased discharge by simple flow expansion.  Because of their position within the network, cascade channels typically are subject to debris flow impacts.  However, in-channel sediment loading from debris slides is often short lived and easily flushed downstream.  Significant morphological changes within these reaches are not expected with normal sediment input from debris slides.

Step pool channels are confined channels with series of cascades and small pools.  High transport capacities enable increased discharges or sediment loads to be transmitted downstream.  As with other confined channels, increased discharge may result in flow width and height expansion without bank cutting or channel down-cutting.  However, changes in pool depth, and thus channel storage are significant morphological changes.  Usually these changes in pool depth are temporary and associated with a decline in the frequency and duration of pool scouring flows or large increases in sediment.  Channel morphology is generally re-established after flood events.

RESPONSE - Response reaches are low gradient, channels in which significant morphologic adjustments occurs in response to increased sediment supply.  Typically, these types of channels are the depositional reaches of stream networks.  Sediment is collected and accumulated in these segments.

Plane Bed channels tend to have planar channel beds with occasional channel spanning rapids.  They are distinguished from step-pool and pool-riffle channels in that they lack rhythmic bedforms.  These channels may lack sufficient flow dynamics to cause pool development except where obstructions such as large wood debris create local pool or bar formation.  These channels occur in confined and unconfined valleys and hence, have a variety of responses to changes in sediment and discharge.  Potential responses include channel widening, incision, bed aggradation, and changes in size of streambed materials.

Pool-riffle channels have a sequence of bars, pools, and riffles and tend to have the widest variety of potential responses.  These channels are generally unconfined, which allows widening in response to either increased discharge or sediment supply.  Increased discharge may also cause bank cutting and meander.  Sediment deposition can occur with higher sediment loads or decreased discharge.  High peak flows can potentially increase the depth of scour and decrease sediment storage.  Less frequent high flows favor pool filling and increased sediment storage.

Regime channels are low gradient, sand-bedded channels exhibiting a succession of bedforms with increasing flow velocity.  Some reaches in gravel and boulder bedded channels also exhibit regime channel characteristics.  With increasing flow velocity bedforms are created in a sequential pattern of planar bed, ripples, sand waves, dunes, high-energy planar bed, and finally antidunes.  In coarser stream beds, bedload migrates in sheets and bedforms are less distinguishable. Regime channels have the lowest relative transport capacities may widen in response to either increased discharge or sediment deposition.  Increased discharge can also result in meandering or channel migration.

Braided channels have a condition of high sediment supply relative to transport capacity.  A significant increase in discharge or decrease in sediment supply may result in conversion to a single thread channel.  Conversely, an increase in sediment deposition may result in further widening of the active channel and development of multiple channels.  Plane bed and regime channels may convert to braided channels with increases in sediment or decrease in discharge.

Table 9.  Hydrologic Properties and Responses

| LTA | Surface Runoff | Channel Density | Stream Flow Duration | Stream Flow Amount | Aquifer Recharge | Stream Types | Stream Reach Processes |
| --- | --- | --- | --- | --- | --- | --- | --- |
| 114 | Low | Low | Intermittent or Perennial | Low flow | Moderate | A, B | Source, Transport |
| 115 | Moderate | Moderate | Intermittent or Perennial | Low flow | Moderate to High | A, B | Source |
| 116 | Low | Low | Intermittent | Occasional storm flow | Low | Low gradient colluvial | Source |
| 117 | Moderate | Moderate | Intermittent or Perennial | Low flow | Low | A, B | Source, Transport |
| 118 | Moderate | Moderate- High | Intermittent | Low flow | Low | Aa, A, B | Source, Transport |
| 124 | Low | Low | Intermittent or Perennial | Low flow | Moderate | A, B | Source, Transport |
| 125 | Moderate | Moderate | Intermittent or Perennial | Low flow | Moderate | A, B | Source |
| 126 | Low | Low | Intermittent | Low flow | Low | Low gradient colluvial | Source |
| 127 | Moderate | Moderate | Intermittent or Perennial | Low flow | Low | A, B | Transport |
| 131 | Low | Moderate | Perennial | High flow | Moderate to High | B, C, D, E | Transport, Response |
| 132 | Flashy | High | Intermittent | Low flow | Low | Aa, A, B | Source, Transport |
| 133 | Low | Moderate | Perennial | High flow | Moderate to High | C, D, E | Response |
| 135 | Moderate | High | Perennial | Flow varies | High | B, C, E | Source, Transport, Response |
| 144 | Low | Low | Intermittent or Perennial | Low flow | Moderate | A, B | Source, Transport |
| 146 | Low | Low | Intermittent | Occasional storm flow | Low | A, B | Source |
| 155 | Moderate | Moderate | Intermittent | Low flow | Moderate | A, B | Source |
| 156 | Low | Low | Intermittent | Occasional storm flow | Low | Low gradient colluvial | Source |
| 157 | Moderate | Low | Intermittent or Perennial | Low flow | Low | A, B | Source, Transport |
| 158 | Flashy | High | Intermittent | Low flow | Low | Aa, A, B | Source, Transport |
| 165 | Moderate | Moderate | Intermittent | Low flow | Moderate | A, B | Source |
| 166 | Low | Moderate | Intermittent | Occasional storm flow | Low | Low gradient colluvial | Source |
| 167 | Moderate | Moderate-High | Intermittent or Perennial | Low flow | Low | A, B | Source, Transport |
| 168 | Moderate | High | Intermittent | Low flow | Low | Aa, A, B | Source, Transport |
| 176 | Low | Low | Intermittent | Occasional storm flow | Low | Low gradient colluvial | Source |
| 177 | Moderate | Low-Moderate | Intermittent or Perennial | Low flow | Low | A, B | Source, Transport |
| 214 | Low | Low | Intermittent or Perennial | Low flow | Moderate | A, B | Source, Transport |
| 215 | Moderate | Moderate | Intermittent | Low flow | Moderate to High | Low gradient colluvial, A, B | Source, Transport |
| 216 | Low | Low | Intermittent | Occasional storm flow | Low | Low gradient colluvial | Source |
| 217 | Moderate | Low-Moderate | Intermittent or Perennial | Low flow | Low | A, B | Source, Transport |
| 218 | Flashy | Moderate-High | Intermittent | Low flow | Low | Aa, A, B | Source, Transport |
| 224 | Moderate | Low | Intermittent or Perennial | Low flow | Moderate | A, B | Source, Transport |
| 226 | Low | Low | Intermittent | Occasional storm flow | Low | Low gradient colluvial | Source |
| 227 | Moderate | Moderate | Intermittent or Perennial | Low flow | Low | A, B | Source, Transport |
| 231 | Low | Moderate | Perennial | High flow | High | B, C, D, E | Transport, Response |
| 232 | Flashy | High | Intermittent | Low flow | Low | Aa, A, B | Source, Transport |
| 233 | Low | Moderate | Perennial | Flow varies | Moderate to High | C, D, E | Response |
| 236 | Low | Moderate-High | Intermittent or Perennial | Low flow | Moderate to High | C, E (low gradient colluvial) | Source, Response |
| 244 | Moderate | Low | Intermittent or Perennial | Low flow | Moderate | A, B | Source, Transport |
| 246 | Moderate | Low | Intermittent | Occasional storm flow | Low | Low gradient colluvial | Source |
| 256 | Low | Low | Intermittent | Occasional storm flow | Low | Low gradient colluvial | Source |
| 257 | Moderate | Low | Intermittent or Perennial | Low flow | Low | A, B | Source, Transport |
| 258 | Flashy | Moderate-High | Intermittent | Occasional storm flow | Low | Aa, A, B | Source, Transport |
| 265 | Low | Moderate | Intermittent | Low flow | Moderate | A, B | Source |
| 266 | Low | Moderate | Intermittent | Occasional storm flow | Low | Low gradient colluvial | Source |
| 267 | Moderate | Moderate-High | Intermittent or Perennial | Low flow | Low | A, B | Source, Transport |
| 268 | Flashy | High | Intermittent | Low flow | Low | Aa, A, B | Source, Transport |
| 273 | Low | Low | Intermittent or Perennial | Flow varies | Moderate to High | B, C, D | Transport, Response |
| 275 | Low | Moderate | Intermittent or Perennial | Low flow | Moderate to High | B, C | Transport, Response |
| 276 | Low | Low | Intermittent | Occasional storm flow | Low | Low gradient colluvial | Source |
| 277 | Moderate | Low-Moderate | Intermittent or Perennial | Low flow | Low | A, B | Source, Transport |
| 315 | Moderate | Moderate | Intermittent | Low flow | Moderate | Low gradient colluvial, A, B | Source, Transport |
| 316 | Low | Low | Intermittent | Occasional storm flow | Low | Low gradient colluvial | Source, Response |
| 317 | Moderate | Low-Moderate | Intermittent | Low flow | Low | A, B | Source, Transport |
| 318 | Flashy | Moderate-High | Intermittent | Occasional storm flow | Low | Aa, A | Source, Transport |
| 326 | Low-Moderate | Low-Moderate | Intermittent | Occasional storm flow | Low | Aa, A | Source, Transport |
| 327 | Flashy | Low-Moderate | Intermittent | Occasional storm flow | Low | Aa, A | Source, Transport |
| 332 | Flashy | High | Intermittent | Low flow | Low | Aa, A, B | Source, Transport |
| 333 | Low | Moderate | Intermittent or Perennial | Flow varies | Moderate to High | C, D | Transport, Response |
| 356 | Low | Low | Intermittent | Occasional storm flow | Low | Low gradient colluvial, A, B | Source, Transport |
| 357 | Moderate | Low | Intermittent | Occasional storm flow | Low | A, B | Source, Transport |
| 358 | Flashy | Moderate-High | Intermittent | Occasional storm flow | Low | Aa, A | Source, Transport |
| 365 | Moderate | Low-Moderate | Intermittent | Low flow | Moderate | A, B | Source, Transport |
| 366 | Low | Low-Moderate | Intermittent | Occasional storm flow | Low | Low gradient colluvial, A, B | Source, Transport |
| 367 | Moderate | Moderate-High | Intermittent | Low flow | Low | A, B | Source, Transport |
| 368 | Flashy | High | Intermittent | Occasional storm flow | Low | A, B | Source, Transport |
| 376 | Low | Low | Intermittent | Occasional storm flow | Low | Low gradient colluvial, A, B | Source, Transport |
| 377 | Moderate | Low | Intermittent | Low flow | Low | A, B | Source Transport |
| 416 | Low | Low | Intermittent | Occasional storm flow | Low | Unknown | Source, Transport |
| 418 | Flashy | Low-Moderate | Intermittent | Unknown | Low | A | Source |
| 432 | Flashy | High | Intermittent | Unknown | Low | Aa, A | Source |
| 433 | Low | Moderate | Perennial | High flow | High | C, D, E | Response |
| 468 | Flashy | High | Intermittent | Unknown | Low | Aa, A | Source |
| 518 | Flashy | Moderate | Intermittent | Occasional storm flow | Low | Aa | Source |
| 532 | Flashy | High | Intermittent | Occasional storm flow | Low | Aa | Source |
| 558 | Flashy | Moderate-High | Intermittent | Occasional storm flow | Low | Aa | Source |
| 567 | Flashy | High | Intermittent | Occasional storm flow | Low | Aa | Source |
| 568 | Flashy | High | Intermittent | Occasional storm flow | Low | Aa | Source |
| 600 | n/a | n/a | n/a | n/a | High | n/a | n/a |
| 736 | Moderate | High | Intermittent or Perennial | Low flow | Moderate to High | C, D, F, E | Response |
| 832 | Flashy | Moderate | Intermittent | Occasional storm flow | Low | Aa | Source |

Sedimentation Processes and Responses

Table 10 lists several geomorphic processes that influence sediment flow in a watershed. Below is a brief description of the information contained in each column of the table.

Soil Erosion (disturbed):  This column contains the interpretation for the potential for surface erosion upon removal of all vegetation material including the forest floor layer.  These conditions often exist after a severe fire that consumes 100% of the forest floor, on an unvegetated road cut/fill slope or on a skid trail.  In these conditions, slope gradients over 15% are generally steep enough to cause serious rill erosion and/or dry ravel.  Erosion ratings are heavily weighted by slope gradient with a slight modification for the resistance or lack of erosion resistance from different soil textures.

LOW (L) - Landtype Associations generally contain site features that limit the probability of sheet erosion.   Generally the site conditions include sufficient rock fragments to armor surfaces, irregular and complex slope shapes with less than 20% gradients, cohesive soils with moderately fine and fine textures, rapid vegetation recovery, and/or surface water runoff is seldom concentrated.

MODERATE (M) - Landtype Associations generally contain site features that limit sheet erosion to rilling.  Erosion control treatments and design is normally required on bare surfaces and is usually adequate in controlling surface erosion.   Generally the site conditions include some rock fragments but insufficient to fully armor the surface, long straight slopes with 20-45% gradients, medium and moderately coarse textured soils, moderately rapid vegetation recovery (2-5 yrs), and/or some probability of concentrated surface runoff.

HIGH (H) - Landtype Associations generally contain site features that develop extensive rilling which can enlarge into gullies.  Special erosion control treatments and design should be a standard practice and may not be totally successful.  Generally the site conditions include long straight slopes with gradients exceeding 45%, coarse to moderately coarse textured soils, vegetation recovery is slow (greater than 5 years), and/or high probability of concentrated surface runoff.

Soil Erosion (undisturbed):  This column contains the interpretation for the potential for surface erosion in a relatively natural setting or lightly disturbance.  The factors used for erosion ratings are slope gradient, understory vegetation cover and type, and field observed duff layers.

LOW (L) - Landtype Associations generally contain site features that limit the probability of sheet erosion.  Generally the site conditions include thick duff layers, dense understory vegetation cover with slope gradients less than 60%, and medium textured surface soil layers.

MODERATE (M) - Landtype Associations generally contain site features that limit sheet erosion to rilling.  Generally the site conditions include the presence of duff layers and some understory vegetation cover with slope gradients ranging from 30- 90%, or  coarse textured soils on slopes between 30-60% with intermittent duff layers and sparse understory vegetation cover; or grass meadows with slopes between 30-60% with surface cover of greater than 70% and medium to moderately coarse soil textures.

HIGH (H) - Landtype Associations generally contain site features that have high natural rates of erosion.  Site factors include slope gradients greater than 60% with moderately coarse or coarse textured soils with a lack of continuous duff layers or understory vegetation cover; areas with a high amount of exposed rock outcrop and low forest canopy cover; and grass meadows with less than 30% ground cover.

Landslide (deep seated):  This column contains the interpretation for the potential for deep seated mass movement.  These landslides have been included in the mapping differentia for LTAs and are the Landform Group – Landslides.  Earth movement is either large masses of slow-moving earth that move along a shear plane deep in the regolith or bedrock or moderate size masses that move along a moderately deep shear plane relatively rapidly but only sporadically.  The relative potential of movement and location varies depending on whether the landslides are ancient features with only unstable margins along active stream courses, dormant features having a higher likelihood of movement when in contact with water tables; and actively moving features.  The hazard rating is constructed to interpret the potential for movement in the worst case situation and at the most unstable location.

A number of complex factors influence deep-seated landslides (Dragovich and Brunengo 1995, Swanson and Swanston 1977, and Sidle 1985).  Many of these site factors were used for developing deep seated landslide hazards.  They are:

1.  easily weathered bedrock high in minerals weathering to clay

2.  geologic structural features such as folding,  faulting, and/or interbedded strata

3.  geomorphic shape features (escarpments and  converging concave topography)

4.  fine textured surficial deposits

5.  slope gradients greater than 20 percent

6.  indications of concentrated ground water

7.  indications of surface and subsurface water

LOW (L) - Landtype Association has very few of the properties associated with landside probability.  Little evidence of landslides has been observed.  The degree of limitation is minor and can be overcome easily.

MODERATE (M) - Landtype Association has properties commonly associated with landslide probability.  These properties occur over a small extent of the area.  Evidence of landslides has been observed but is not common. The degree of limitation can usually be overcome by special planning, design, or maintenance.

HIGH (H) - Landtype Association has most of the properties associated with landslide probability.  Evidence of landslides has been observed over most of the area.  The degree of limitation generally requires major reclamation, special design, or intensive maintenance.

Landslide (shallow rapid):  This column contains the interpretation for the potential for shallow rapid landslides.  These landslides tend to originate on very steep landforms where a complex of pockets of deep soils usually in colluvial channels are in complex with shallow soils and bedrock.  The landform, Canyons, is the most representative of this landform/soil condition.  The frequency and rate of these landslides varies with climatic regimes.  In the Blue Mountains, the natural frequency would be likely associated with storm events that exceed 100 year storm events.  Roads and harvest have the potential to accelerate natural rates and frequency.

A number of complex factors influence shallow-rapid landslides (Dragovich and Brunengo 1995, Sidle 1985, Swanston 1970 and 1974, Wu & Swanston 1980).  Many of these site factors were used for developing deep seated landslide hazards.  They are:

1.  slope gradients greater than 40%

2.  convergent drainages and/or catchment basins

3.  unconsolidated coarse textured soils

4.  interface of materials with discontinuous hydrologic properties

5.  sparse vegetation patterns

6.  geomorphic features (debris chutes associated with debris cones or alluvial fans)

7.  high low order drainage density especially with parallel patterns

LOW (L) - Landtype Association has very few of the properties associated with landside probability.  Little evidence of landslides has been observed.  The degree of limitation is minor and can be overcome easily.

MODERATE (M) - Landtype Association has properties commonly associated with landslide probability.  These properties occur over a small extent of the area.  Evidence of landslides has been observed but is not common. The degree of limitation can usually be overcome by special planning, design, or maintenance.

HIGH (H) - Landtype Association has most of the properties associated with landslide probability.  Evidence of landslides has been observed over most of the area.  The degree of limitation generally requires major reclamation, special design, or intensive maintenance.  Accelerated sedimentation is likely to occur even with special management practices.

Sediment Delivery Efficiency:  This column contains the interpretation of the relative efficiency of landforms to route eroded debris into first order stream channels and deliver sediment into mainstem streams.  The factors used to rate Landtype Associations are:  surface runoff response, slope gradient and shape, low order stream density, stream channel geomorphic type; position in the watershed in terms of distance to a mainstem perennial channel; and potential for shallow rapid landslides.  This interpretation excludes the sediment delivery processes associated with streambanks and toeslopes along mainstems as it is a site-scale interpretation not landscape level interpretation.

LOW (L) - Landscapes can absorb a great deal of surface water before individual soil particles are detached.  Surface runoff normally is well dispersed and does not become concentrated in first order streams.  Landtype Association features limit surface water and sediment from being routed quickly to first order stream systems.  First order stream catchment basins do not have evidence of rilling and channels do not have a history of scour or non-vegetated deposition.  Normally these Landtype Associations have not had a history of shallow rapid landslides being delivered into mainstem streams.  Usually Landtype Associations have a set of the following site features:  low slope gradients <25%, more than 80 percent vegetation cover; deep, moderately coarse textured regoliths; very little exposed bedrock; low drainage density first order streams; area not normally exposed to rain-on-snow events or high intensity rainstorms.

MODERATE (M) - Landscapes absorb some surface water before individual soil particles are detached.  Surface runoff is somewhat well dispersed but some concentrated flows are routed into first order drainages.  Landtype Association features are somewhat efficient in routing surface water and sediment into first order stream systems.  First order stream catchment basins have some evidence of past rilling and stream channels have some evidence of scour.  Slope shapes are complex with breaks in slope gradient that offer slope storage of eroding debris prior to reaching stream channels.  Usually Landtype Associations have a set of the following site features:  slope gradients between 25 and 45 percent; vegetation cover is 30 to 80 percent; regolith depths that vary from shallow to moderately deep; exposed bedrock is less than 25 percent of the area; moderate drainage density of confined or entrenched first order stream systems with both source and transport stream types; area exposed to infrequent rain-on-snow events or high intensity rainstorms.

HIGH (H) - Landscapes do not absorb a great deal of surface water before individual soil particles detach.  Surface runoff is poorly regulated and concentrated flows are routed rapidly into first order drainages.  Landtype Association features are extremely efficient in routing surface water and sediment into first order stream systems.  Slope shapes are less complex with few breaks in grade to offer slope storage of eroding debris.  First order catchment basins have evidence of past rilling and stream channels have evidence of scour or non-vegetated deposition.  Normally these Landtype Associations have had a relatively frequent history of shallow rapid landslides or high incidence of source type, colluvial channels deliver directly into mainstem streams.  Usually Landtype Associations have a set of the following site features:  steep slope gradients (45%+); less than 30 percent vegetation cover; shallow regoliths; exposed bedrock exceeds 25 percent of the area; high drainage density of confined or entrenched first order streams; area is exposed to frequent rain-on-snow events or high intensity rainstorms.

Table 10:  Sedimentation Properties and Responses

| LTA | Sediment Delivery Efficiency | Soil Erosion (Disturbed) | Soil Erosion (Undisturbed) | Landslides Deep-Seated | Landslides Shallow-Rapid |
| --- | --- | --- | --- | --- | --- |
| 114 | L-H | H | L | M | M |
| 115 | L-M | M-H | L | L-M | L |
| 116 | L | L-M | L | L | L |
| 117 | M | H | L | L-M | M |
| 118 | H | H | M | L-M | H |
| 124 | L-H | L-H | L | H | L |
| 125 | L-M | L-M | L | H | L |
| 126 | L | L | L | M | L |
| 127 | M | M-H | L | M-H | L |
| 131 | L | L-M | L | L-M | L |
| 132 | H | M-H | L-H | L-M | M-H |
| 133 | L-H | L | L | L | L |
| 135 | L-M | M-H | L | L-M | L |
| 144 | L | M | L | H | L |
| 146 | L | L | L | M | L |
| 155 | L-M | H | M | M-H | L |
| 156 | L | M-H | L | L | L |
| 157 | M | H | M | M | L |
| 158 | H | H | H | M | H |
| 165 | L-M | M-H | L | M | L |
| 166 | L | L-M | L | L | L |
| 167 | M | H | L | L-M | M |
| 168 | H | H | M | M-H | H |
| 176 | L |  | L | L-M | L |
| 177 | M | H | L | M-H | L |
| 214 | L-H | L-H | L-M | M-H | L |
| 215 | L-M | M-H | M | L-M | L |
| 216 | L | L-M | L | L | L |
| 217 | M | H | L-M | L | L |
| 218 | H | H | M | L | H |
| 224 | L-M | L-H | L | H | L |
| 226 | L | L-M | L | L-M | L |
| 227 | M | M-H | L | M-H | M |
| 231 | L | M-H | L | L | L |
| 232 | H | M-H | L-H | L-M | M-H |
| 233 | L-H | L | L | L | L |
| 236 | L | L-M | L | L | L |
| 244 | L-H | L-H | L | H | L |
| 246 | L | L-M | L | M | L |
| 256 | L | L-M | L | L | L/L |
| 257 | M | H | M-H | M | M-H |
| 258 | H | H | M | M | H |
| 265 | L | H | L | L-M | L |
| 266 | L-M | M | L-M | L | L |
| 267 | M | H | M | L-M | M |
| 268 | H | H | M-H | M | H |
| 273 | L-H | L | L | L | L |
| 275 | L-M | L | L | L | L |
| 276 | L | M | L | M | L |
| 277 | M | H | L | M-H | L |
| 315 | L-M | M-H | L-M | L | L |
| 316 | L | L-M | L-M | L | L |
| 317 | M | M-H | M | L | L |
| 318 | H | H | H | M | H |
| 326 | L | M | L-M | L |  |
| 327 | M | H | M | M | L |
| 332 | H | M-H | L-H | M | H |
| 333 | L-M | L | L | L | L |
| 356 | L | M | L-M | L-M | L |
| 357 | M | H | M-H | L-M | M |
| 358 | H | H | H | L-M | H |
| 365 | L | M-H | L-M | L-M | L |
| 366 | L | L-M | L-M | L | L |
| 367 | M | H | L | L-H | L-M |
| 368 | H | H | H | M-H | H |
| 376 | L | L-M | L-M | L | L |
| 377 | M | H | M | M | L |
| 416 | L | M | L-M | L | L |
| 418 | H | H | M | M | H |
| 432 | H | M-H | L-H | L | M-H |
| 433 | L-H | L | L | L | L |
| 468 | H | H | M | M-H | H |
| 518 | H | H | H | M | H |
| 532 | L-H | M-H | L-H | M | H |
| 558 | H | H | H | M | H |
| 567 | H | H | L | L |  |
| 568 | H | H | H | L | H/H |
| 736 | L-H | L-M | M | L | M |
| 832 | M-H | H | H | L | M |

Fish and Wildlife Habitat

Table 11 contains the Wildlife and Fish Potential Habitat and Responses for each Landtype Association.  Listed below is a brief description of the information contained in each column of the table.

Unique Habitat Features:  This column contains some of the site properties that provide important habitat components for some wildlife species.  The presence or absence of these properties is normally linked to geomorphic expression.  They were identified on aerial photographs at 1 inch equals one mile scale (1:63,360) and observations were supported by field experience of the mapping team.  In some cases, site features, not easily seen on aerial photographs were inferred through processes or site-scale landforms that are associated with geomorphic expression.  For example, larger seeps are identifiable by vegetation type and pattern.  Exact locations of smaller seeps may not be seen on aerial photography but can be inferred through extrapolation of known slope configuration and groundwater movement controlled by a landform, its typical position and geomorphic history in a watershed, and/or geology group.  Some glacial landforms are highly predictable in this regard, in that, glacial deposits often occur along or at the toe of steep sideslopes where groundwater is intercepted.

Potential Lynx Habitat:  This column contains an interpretation of the quality of habitat for potential Lynx habitat in each Landtype Association.  The interpretation is for potential and not existing habitat quality.  Potential habitat is important because the natural role of fire disturbance will likely alter present and future habitat quality.  The highest quality habitat is associated with forests with a structure that includes branches low to the ground; has persistent winter snow with depths exceeding 2 feet; and slope gradients less than about 30 percent.  Lodgepole pine seral forests within the subalpine fir series offer the greatest potential for the largest contiguous area having the first two listed habitat features.  Although, other series have lodgepole pine seral forests and other associated factors such as snow depth and forest structure, they usually lack consistent presence over large land area and hence, have less potential to provide contiguous quality habitat.  Potential Natural Vegetation (PNV) was used to predict potential for forest type and structure components and geomorphic expression or landform was used to interpret slope gradient.

Travel corridors are an important component of Lynx habitat.  Again, interpretation ratings are in terms of potential not existing.  The criteria used in this interpretation are: continuous slope gradients less than 30 percent on landforms with persistent winter snow.

VERY HIGH (VH) - Landtype Associations contain a preponderance of subalpine fir series and landforms with slope gradients less than 30 percent.

VERY HIGH (VHT) - Landtype Associations contain very high quality habitat as well as possible major travel corridors.  Units contain a preponderance of subalpine fir series and consist of broad gently rolling ridge tops with slopes generally less than 30 percent.

HIGH (H) - Landtype Associations contain subalpine fir series and landforms with slope gradients generally less than 30 percent; however some slopes exceed 30 percent.

MODERATE (M) - Landtype Associations contain subalpine fir series and landforms with slope gradients that generally exceed 30 percent; however inclusions of slope gradients less than 30% may occur.

LOW (L) - Landtype Associations contain moist Douglas-fir, grand fir, and western redcedar/hemlock series and have landforms with slope gradients generally less than 30 percent; however, some slopes exceed 30 percent.

VERY LOW (VL) - Landtype Associations contain moist Douglas-fir, grand fir, and western redcedar/hemlock series and have landforms with slope gradients that generally exceeding 30 percent; however, some slopes are less than 30 percent.

Potential Wolverine Denning Habitat:  This column contains an interpretation of the quality for wolverine denning habitat in each Landtype Association.  The criteria or factors used to help develop denning habitat are as follows:  aspect; relief; elevation, presence of boulder talus, and snow depth and persistence during denning season (Copeland 1996).  Only HIGH and MODERATE quality ratings are displayed.  Those Landtype Associations without a rating should be considered to have low quality denning habitat.

HIGH (H) - All site features for high quality denning habitat exist in the Landtype Association.  Landtype Associations are on north or northeast aspects; have boulder talus slopes; are above 5500 feet elevation and have at least moderate depths of winter snow; and have concave to flat slope configuration.  Cirque basins contain all of these site features.

MODERATE (M) – Some but not all of the site qualities associated with denning habitat is present in the Landtype Association.  Typically, these LTAs include some boulder talus but may not include all of the other important site properties such as aspect, relief, and elevation features.

Mule Deer Winter Range:  This column contains the relative interpretation of the quality for mule deer winter range in each Landtype Association.  The criteria or factors used to help identify mule deer winter range habitat are as follows: southern exposures; slope; elevation zone linked to low snow-fall areas, vegetation zones, and adjoining security areas.  Only HIGH and MODERATE ratings are displayed.  All other Landtype Associations would be considered to have low quality Mule Deer Winter Range.

HIGH (H) – Landtype Associations consist of the following:  south-facing aspects with ponderosa pine and shrub-steppe potential natural vegetation; slopes are generally below 3500 feet in elevation; and slope gradients are greater than 30 percent.  These south facing slopes are adjacent to north-facing slopes that support dense canopied forests within the Douglas-fir series that provide thermal cover.

MODERATE (M) - Landtype Associations that generally lack the ponderosa pine vegetation zone component but include all the other winter range factors or criteria.

Security Cover (S) – Landtype Associations have a high potential to provide security cover in close association with mule deer winter range.  Landtype Association features used to indicate potential security cover are:  potential natural vegetation series which support multi-layered dense forests that provide vegetative screening; and landforms associated with narrow canyons or with a high complexity of dissection or change in slope shape that reduces distance of line of sight.

Mountain Goat Habitat:  This column contains the relative interpretation of the quality for Mountain Goat Habitat in each Landtype Association.  The criteria or factors used to help identify mountain goat habitat are as follows:  avalanche chutes; scree or talus slopes, slope gradients exceeding 75 percent; abundant bedrock exposures; alpine meadows, and timber-line vegetation zones.  Only HIGH and MODERATE quality ratings are displayed.  All the other Landtype Associations would be considered to have low quality mountain goat habitat.

HIGH (H) - Landtype Associations that contain all of the habitat features associated with high quality habitat such as; avalanche chutes, scree and talus slopes, slopes greater than 75 percent, abundant bedrock exposures, alpine meadows, and timber line forest zones (subalpine and mountain hemlock vegetation zones).

MODERATE (M) - Landtype Associations that contain many but not all of the habitat features associated with high quality habitat.  The missing features significantly reduce the quality of habitat.

WINTER RANGE (W) - Landtype Associations that contain all of the habitat features association with high quality winter range, such as; slopes greater than 75 percent, abundant bedrock exposures, winter snow depths less than two feet, security cover vegetation; southern exposures or vegetation zones that represent warm dry conditions; and foraging habitat associated with Douglas-fir/ponderosa pine potential natural vegetation zones.

Bull Trout Spawning/Rearing:  This column contains the relative interpretation of potential spring upwelling areas along stream channels within each Landtype Association.  Spring upwelling tends to help maintain adequate stream flow and moderates water temperatures (Baxer and Hauer 2000).   Site factors used to identify potential upwelling areas include:  thick, unconsolidated glacial drift deposits occurring below prominent "rocky" ridges; concave slope relief normally characteristic of U-shaped glacial valleys; stream segments bounded by alluvial fans in valley bottom positions; mainstem channel morphology interrupted by bedrock nick-points; and known spring upwelling areas identified by field observations.  Only HIGH and MODERATE ratings are displayed.  All the other Landtype Associations would be considered to have low probability for spring upwelling.

HIGH (H) - Landtype Associations contain all features associated with spring upwelling that may produce high quality bull trout spawning/rearing habitat.  The site features include:  thick, unconsolidated glacial drift deposits; glacial drift deposits occur below prominent "rocky” ridges; concave slope relief characteristic of U-shaped glacial valleys; stream segments that are bounded by coalescing alluvial fans; and occasional bedrock nick-points in the valley floor.

MODERATE (M) - Landtype Associations that contain many but not all of the features associated with spring upwelling that may produce quality of bull trout spawning/rearing.  Site features include:  glacial drift deposits but are not found in glacial U shape valleys and are not associated with upper "rocky" ridges.

Table 11.  Fish and Wildlife Habitat

| LTA | Seeps | Ponds | Streams | Cliffs | Talus | Avalanche chutes | Wet Meadow | Grassland | Lynx Habitat | Wolverine Denning | MuleDeer Winter Habitat | Mountain Goat | Moose | Trout Spawn Rearing |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |
| 114 | High |  |  |  |  |  | Moderate |  |  |  |  |  |  |  |
| 115 | Low |  |  |  |  |  | High |  | High Travel |  |  |  |  |  |
| 116 |  |  |  |  |  |  |  |  | High Travel |  |  |  |  |  |
| 117 | Low |  |  | Moderate |  |  |  |  | Moderate |  | Moderate Security |  |  |  |
| 118 |  |  |  | High | Moderate |  |  |  | Moderate |  | Moderate Security |  |  | Moderate |
| 124 | High |  |  |  |  |  | Moderate |  | High |  |  |  |  |  |
| 125 | Low |  |  |  |  |  | Moderate |  | High |  |  |  |  |  |
| 126 |  |  |  |  |  |  |  |  | High Travel |  |  |  |  |  |
| 127 | Moderate |  |  | Moderate |  |  |  |  | Moderate |  |  |  |  |  |
| 131 | Moderate | High |  |  |  |  | High |  | Very High | High |  |  | High | High |
| 132 |  |  |  | High | High | High |  |  | Very High | High |  | Moderate |  |  |
| 133 |  |  | High |  |  |  | High |  | High |  |  |  | Moderate | High |
| 135 |  |  | High |  |  |  | Moderate |  | Moderate | High |  |  |  | Moderate |
| 144 | High |  |  |  |  |  |  |  | Moderate |  |  |  |  |  |
| 146 | Low |  |  |  |  |  |  |  | Moderate |  |  |  |  |  |
| 155 |  |  |  |  |  |  |  |  | Moderate |  |  |  |  |  |
| 156 |  |  |  |  |  |  |  |  | High Travel |  |  |  |  |  |
| 157 |  |  |  |  |  |  |  |  | High |  |  |  |  |  |
| 158 |  |  |  | Moderate | High |  |  |  |  |  |  |  |  |  |
| 165 |  |  |  |  |  |  |  |  |  |  |  |  |  |  |
| 166 |  |  |  |  |  |  |  |  | Moderate Travel |  |  |  |  |  |
| 167 |  |  |  |  |  |  |  |  | Moderate |  | Moderate Security |  |  |  |
| 168 |  |  |  |  |  |  |  |  |  |  | Moderate Security |  |  |  |
| 176 |  |  |  |  |  |  |  |  |  |  |  |  |  |  |
| 177 |  |  |  |  |  |  |  |  |  |  |  |  |  |  |
| 214 | High |  |  |  |  |  | Moderate |  | Low |  |  |  |  |  |
| 215 | Low |  |  |  |  |  | Moderate | Moderate | Low |  |  |  |  |  |
| 216 |  |  |  |  |  |  |  |  | Low |  |  |  |  |  |
| 217 |  |  |  | Moderate |  |  |  | Moderate |  |  | High Security |  |  |  |
| 218 |  |  |  | High | High |  |  | Moderate |  |  | High Security |  |  | Moderate |
| 224 | High |  |  |  |  |  | Moderate |  |  |  |  |  |  |  |
| 226 |  |  |  |  |  |  |  | Moderate |  |  |  |  |  |  |
| 227 | Moderate |  |  |  |  |  |  | Moderate |  |  | High Security |  |  |  |
| 231 | Moderate |  | High |  |  |  | High |  | Moderate | High |  |  | High | High |
| 232 |  |  |  | High | High | High |  |  |  | High |  | Moderate |  |  |
| 233 |  |  | High |  |  |  |  |  | Moderate |  |  |  |  | High |
| 236 |  |  |  |  |  |  |  |  | Moderate |  |  |  |  |  |
| 244 | High |  |  |  |  |  | Moderate |  |  |  |  |  |  |  |
| 246 |  |  |  |  |  |  |  | Moderate |  |  |  |  |  |  |
| 256 |  |  |  |  |  |  |  |  | Low |  |  |  |  |  |
| 257 |  |  |  |  |  |  |  |  | Low |  |  |  |  |  |
| 258 |  |  |  | High | High |  |  |  |  |  |  |  |  |  |
| 265 |  |  |  |  |  |  |  |  |  |  |  |  |  |  |
| 266 |  |  |  |  |  |  |  |  | Low |  |  |  |  |  |
| 267 |  |  |  |  |  |  |  |  | Low |  | High Security |  |  |  |
| 268 |  |  |  | Moderate | Moderate |  |  |  |  |  | High Security |  |  |  |
| 273 |  |  | High |  |  |  | Moderate | Moderate |  |  |  |  |  |  |
| 275 |  |  |  |  |  |  |  |  |  |  |  |  |  |  |
| 276 |  |  |  |  |  |  |  |  |  |  |  |  |  |  |
| 277 |  |  |  |  |  |  |  |  |  |  | High Security |  |  |  |
| 315 |  |  |  |  |  |  | Moderate | High |  |  |  |  |  |  |
| 316 |  |  |  |  |  |  |  | High |  |  |  |  |  |  |
| 317 |  |  |  | Moderate |  |  |  | High |  |  | High |  |  |  |
| 318 |  |  |  | High | High |  |  | High |  |  | High |  |  |  |
| 326 |  |  |  |  |  |  |  | High |  |  |  |  |  |  |
| 327 |  |  |  |  |  |  |  | High |  |  | High |  |  |  |
| 332 |  |  | High |  |  | High | High | High |  |  |  | Moderate |  |  |
| 333 |  |  | High |  |  |  | Moderate | High |  |  |  |  |  | Moderate |
| 356 |  |  |  |  |  |  |  | High |  |  |  |  |  |  |
| 357 |  |  |  |  |  |  |  | High |  |  | High |  |  |  |
| 358 |  |  |  | High | High |  |  | High |  |  | High |  |  |  |
| 365 |  |  |  |  |  |  |  | High |  |  |  |  |  |  |
| 366 |  |  |  |  |  |  |  | High |  |  |  |  |  |  |
| 367 |  |  |  |  |  |  |  | High |  |  | High |  |  |  |
| 368 |  |  |  | Moderate | High |  |  | High |  |  | High |  |  |  |
| 376 |  |  |  |  |  |  |  | High |  |  |  |  |  |  |
| 377 |  |  |  |  |  |  |  | High |  |  | High |  |  |  |
| 416 |  |  |  |  |  |  | Moderate |  |  |  |  |  |  |  |
| 418 |  |  |  | High | High |  |  |  |  |  | Moderate |  |  |  |
| 432 |  | Moderate |  |  |  |  |  |  |  |  |  |  |  |  |
| 433 |  |  | High |  |  |  | High |  |  |  |  |  | Moderate | High |
| 468 |  |  |  | Moderate | High |  |  |  |  |  |  |  |  |  |
| 518 |  |  |  |  |  |  |  |  |  |  | High |  |  |  |
| 532 |  |  |  | High | High | High | High |  |  | Moderate |  | High |  |  |
| 558 |  |  |  |  | High |  |  |  |  |  | High |  |  |  |
| 567 |  |  |  |  | Moderate |  |  |  |  |  | High |  |  |  |
| 568 |  |  |  | High | High |  |  |  |  |  | High |  |  |  |
| 736 |  |  | Moderate |  |  |  | High | High |  |  |  |  | Moderate | Moderate |
| 832 |  |  |  | High | Moderate | Moderate |  | High | Moderate | Moderate |  | High |  |  |

Vegetation Properties and Response

Table 12 contains the vegetation properties and responses for each Landtype Association.  Listed below is a brief description of the information contained in each column.

Vegetation Zone:  This column contains the potential natural vegetation group which is an aggregation of Plant Association Groups (PAG).  Each zone represents a unique and contrasting ecological processes that influence productivity, understory and overstory density, and recovering from disturbance.  For further explanation on composition and how these categories were constructed consult Parts I and II of this report.

Non-Forest Area (%):  This column lists the estimated average area with non-forest.  Non-forest represented is comprised of grass, shrub or rock.  Non-forest area was estimated using the initial vegetation layer, Landtype Phase which mapped complexes and individual map units of non-forest areas.  The Landtype Phase map was created from various sources of existing vegetation mapping and plant association classifications from stand exam data.

Vegetation Zone (Wood Fiber) Productivity:  This column lists ratings for vegetation zones using Forest Productivity Classes as listed in Appendix E, “Plant Associations of the Blue and Ochoco Mountains” by Charles Grier Johnson, Jr. and Rodrick R. Clausnitzer (Johnson and Clausnitzer 1992).  The most common plant associations observed to occur in each Vegetation Zone was used to apply productivity classes.  Ranges of productivity are given when the Vegetation Zone encompasses a large range of different plant associations and corresponding productivity.  Ratings relate to the measure for average annual basal area growth and are as follows:

VL:  Very Low - <20 cubic feet/acre/year

L:    Low - 20-30 cubic feet/acre/year

M    Moderate - 40-50 cubic feet/acre/year

H:   High - 86-120 cubic feet/acre/year

VH: Very High - >121 cubicfeet/acre/year

Inherent Soil Productivity:  This column contains an interpretation of soil productivity as it influences overall forest productivity.  The purpose of this interpretation is to provide a rating that can be used in association with Forest Productivity Classes to reflect an overall concept of productivity for each Landtype Association.  This rating is provided in absence of actual site productivity data associated directly to each Landtype Association.

The principal soil properties used in this rating are soil depth, soil texture as it relates to water holding capacity, clay percent as it relates to cation exchange capacity, and general soil climate.

The ratings suggest whether the particular LTA is on the “low, mid, or high end” of the range given for a Forest Productivity Class as referenced in the prior rating column. More than rating reflects a complex of soils with distinctly different soil properties.  Ratings are explained below:

VERY LOW (VL) – Site productivity is likely at the lowest end of the range of potential productivity for a given plant association group.  The soil regolith has a relatively very low water holding capacity and nutrient availability due to coarse to moderately coarse textures with a high amount of coarse sands in the soil matrix, and/or severe moisture stress or cold temperatures limiting biological processes; and/or shallow soil depth and a high amount of bedrock exposure severely influences water or nutrient capacity.

LOW (L) - Site productivity is likely at the low end of the range of potential productivity for a given plant association group.  The soil regolith has a relatively low water holding capacity and nutrient availability due to moderately coarse textures or somewhat finer textures that have limited biological processes due to cold temperatures or moisture stress or limited capacity due to shallow soil depths and a high amount of bedrock exposure.

MODERATE (M) - Site productivity is likely in the middle of the range of potential productivity for a given plant association group. The soil regolith has relatively moderate water holding capacity and nutrient availability due to moderately coarse to medium textures from geology parent materials that produce fine sands and silts in the matrix.  Coarser, sandier soil textures are included when soils have a volcanic ash mantle or loess surface layer which substantially enhances productivity.  Somewhat finer textures are included when it is expected that biological processes are limited due to cold temperatures or capacity is limited due to shallow soil depths and a high amount of bedrock exposure.

HIGH (H) - Site productivity is likely at the high or very high end of the range of potential productivity for a given plant association group.  The soil regolith has a relatively high water holding capacity and nutrient availability due to moderately fine to fine textures.  Most soils have a volcanic ash mantle that enhances productivity.  Biological processes are not typically limited by cold temperatures.

LTA Forest (Wood Fiber) Productivity:  This column contains the synthesis of the two columns, Vegetation Zone Productivity and Inherent Soil Productivity.  The ratings listed estimate the potential productivity for the Landtype Association.  Considered in the rating are the following: 1) plant associations are integrators of site factors that influence vegetation composition and diversity and relative productivity; and 2) specific soil properties have a direct influence on site productivity and a direct relationship to a given area’s productivity.  Ratings are defined as follows:

VL:  Very Low - <20 cubic feet/acre/year

L:    Low - 20-30 cubic feet/acre/year

M    Moderate - 40-50 cubic feet/acre/year

H:   High - 86-120 cubic feet/acre/year

VH: Very High - >121 cubicfeet/acre/year

Herbage Production (air-dry/acre/yr):  This column contains an estimate of forage production in the forest understory and on grasslands.  Forage as defined for this rating includes forbs, grasses, and sedges.  The ratings reflect an average range of production as extrapolated from clipping data (air-dry/acre/yr) for soil series and plant associations, respectively, from Umatilla County Soil Survey (USDA NRCS 1988) and Plant Associations of the Blue and Ochoco Mountains (Johnson and Clausnitzer 1992).  This interpretation should be used to help compare herbage production between Landtype Associations and not as an absolute level of production.  Annual production can vary greatly from year to year as precipitation amount and distribution varies.  The production figures cited below are for an average to above average precipitation year.

VERY LOW (L) - Herbage production is less than 300 pounds of air dry weight per year.  Landtype associations generally contain site features that infer very low productive conditions for herbage.  Generally the area contains one or more of the following conditions:  dense multi structured forest canopies; very shallow, rocky soils, soils easily eroded; and forest understories dominated by low and mid-level woody shrubs.  Normally natural openings are a result of disturbance and are often dominated by mid to tall woody shrubs.

LOW (L) - Herbage production ranges from 300 to 500 pounds of air dry weight per year.  Landtype associations generally contain site features that infer low productive conditions for herbage.  Generally the area contains one or more of the following conditions:  upper elevation alpine conditions; shallow grassland soils; relatively dense forest canopies; and forest understories dominated by low growing woody shrubs with some grasses.

MODERATE (M) - Herbage production ranges from 500 to 1000 pounds of air dry weight per year.  Landtype associations generally contain site features that infer moderate or intermediate productive conditions for herbage.  Generally the area contains one or more of the following conditions:  open to partially closed, single-storied forest canopies; moderately deep grassland soils; and forest understories dominated by a mixture of grasses, forbs, and low growing woody shrubs.

HIGH (H) - Herbage production normally exceeds 1000 pounds of air dry weight per year.  Landtype Associations generally contain site features that infer highly productive conditions for herbage.  Generally the area contains one or more of the following site conditions:  open meadows with only scattered coniferous trees; ground cover is dominated by a mixture of grasses, forbs, and sedges and/or grasslands associated with warm low level shrubs (juniper, bitterbrush and sagebrush); medium to moderately fine textured; depth of bedrock is greater than two feet; intermediate or subirrigated areas creating wet meadows or moist grasslands.

Understory and Overstory Vegetation Recovery:  This column contains the interpretation for vegetation to regenerate after disturbance to support ground cover or pre-disturbance forest densities.  The most common disturbance interpreted for is wildfire.  Disturbance conditions considered are those where the forest floor is removed and the surface soil layer is exposed in forests and in meadows, vegetation is consumed to root crowns.

Site factors used to develop this interpretation include: harsh climatic conditions; moisture stress; soil erosion hazard; and unique soil regoliths such as from serpentine geology.   Harsh climatic conditions are associated with subalpine/alpine elevations and support subalpine fir or whitebark pine or the Parkland Vegetation Zone.  These high elevations have short growing seasons or are exposed to desiccation by winds that limit plant growth.  Moisture stress conditions are generally associated with a set of the following conditions:  shallow surface horizons over coarse textured, bouldery regoliths; southern exposures; and low elevations were moisture and heat stress can affect seedling establishment.  Moisture stress can occur in upper elevations associated with wind desiccation.  Geologic features such as serpentine soils may produce soil chemical and physical properties that that hinder regeneration (Walker 1954).

VERY LOW (VL) - Site features generally cause extreme limitations for herbaceous vegetation and shrubs to regenerate and occupy sites or for seeds to germinate.  Very harsh climatic conditions or soil/site features create extreme moisture stress, chronic erosion, or geologic features inhibit regeneration and vegetation establishment.  Vegetation establishment is very slow and conditions may not sustain several pre-disturbance species.  These site features are predominant in the area.

LOW (L) - Landtype Association contain site features that generally create limitations for herbaceous vegetation and shrubs to regeneration or for seeds to germinate. Harsh climatic conditions or soil/site features that create moisture stress, erosion, or geologic features limit regeneration.  Vegetation establishment is slow and species diversity is limited for tens of years.  These site features predominate throughout the area.

MODERATE (M) - Landtype Association generally contains soil or site features that create some limitations for herbaceous vegetation and shrubs to regenerate or for seeds to germinate.  Vegetation occupies the site but competition for moisture or light may inhibit species diversity.  Forests may be slow to reach pre-disturbance density. These site features are common but do not occur throughout the area.

HIGH (H) - Landtype Association generally contain site and soil features that do not limit herbaceous vegetation and shrubs from regenerating or seeds from germinating.  Vegetation readily re-occupies the site with many pre-disturbance species represented.  Forests regenerate readily to often higher than pre-disturbance density.

Table 12.  Vegetation Properties and Responses

| LTA | Vegetation Zone | Nonforest Area (%) | Vegetation Zone Productivity | Inherent Soil Productivity | LTA Forest Productivity | Herbage Production | Understory Recovery | Overstory Recovery |
| --- | --- | --- | --- | --- | --- | --- | --- | --- |
| 114 | Moist Forest | 0-10 | M-VH | H | H,VH | L | M-H | H |
| 115 | Moist Forest | 0-10 | M-VH | H | H,VH | L | M-H | H |
| 116 | Moist Forest | 0-10 | M-VH | H | VH,H,M | L | M-H | H |
| 117 | Moist Forest | 0-10 | M-VH | H | H,MH,VH | L | M-H | H |
| 118 | Moist Forest | 10-20 | MH-VH | H | MH,M | L | M | H |
| 124 | Moist Forest | 0-10 | MH-VH | H | VH,H | L | M-H | H |
| 125 | Moist Forest | 0-10 | MH-VH | H | VH,H | L | M-H | H |
| 126 | Moist Forest | 0-10 | MH-VH | H | VH,H | L | M-H | H |
| 127 | Moist Forest | 0-10 | MH-VH | H | H,VH | L | M-H | H |
| 131 | Moist Forest | 0-10 | M-VH | H | H,VH,M | L | M-H | L-H |
| 132 | Moist Forest | 10-20 | VL-H | L,M | M,VL | L | L-M | L-H |
| 133 | Moist Forest | 0-10 | M-VH | M | H,M,VH | L | M-H | H |
| 135 | Moist Forest | 0-10 | M-H | VL, H | H,M,VL | L | H | H |
| 144 | Moist Forest | 0-10 | MH-VH | H | VH | L | H | H |
| 146 | Moist Forest | 0-10 | MH-VH | H | VH | L | H | H |
| 155 | Moist Forest | 0-10 | M-VH | M | H | L | M | H |
| 156 | Moist Forest | 0-10 | M-VH | M | H,VH,M | L | L-M | H |
| 157 | Moist Forest | 0-10 | M-H | M | H,M,VH | L | L-M | H |
| 158 | Moist Forest | 0-10 | M-H | M | M | L | L-M | H |
| 165 | Moist Forest | 0-10 | M-H | M | H | L | M | H |
| 166 | Moist Forest | 10-20 | M-VH | M | M,VH | L | M | H |
| 167 | Moist Forest | 10-20 | MH-VH | M | VH,H | L | M | H |
| 168 | Moist Forest | 10-20 | MH-VH | M | H,VH | L | L-M | H |
| 176 | Moist Forest | 0-10 | M-VH | M | M | L | M | H |
| 177 | Moist Forest | 0-10 | MH-VH | M | M | L | M | H |
| 214 | Dry Forest | 0-10 | M-H | MH | M,H | H | M-H | M |
| 215 | Dry Forest | 20-30 | M | MH | ML,M | MH | M-H | M |
| 216 | Dry Forest | 20-30 | M-H | VL,M | VL, M | M-MH | M-H | M |
| 217 | Dry Forest | 20-30 | M-H | M | M,H | M-MH | M-H | L-M |
| 218 | Dry Forest | 30-40 | VL-M | VL,MH | L,M,VL | M | M | L-M |
| 224 | Dry Forest | 10-20 | M | H | M,H | MH-H | M-H | M |
| 226 | Dry Forest | 10-20 | M-MH | H | M,MH | MH-H | M-H | M |
| 227 | Dry Forest | 20-30 | M-H | H | H | MH-H | M-H | L-M |
| 231 | Dry Forest | 20-30 | M-VH | M | MH,VH | ML-M | H | L-M |
| 232 | Dry Forest | 30-40 | VL-VH | VL, H | VH,VL | L | L-M | L-H |
| 233 | Dry Forest | 10-20 | M | M | M | MH-H | H | H |
| 236 | Dry Forest | 30-40 | M | M | M | MH-H | H | M |
| 244 | Dry Forest | 10-20 | M | MH | M | MH-H | H | M |
| 246 | Dry Forest | 10-20 | M | MH | M | MH-H | M-H | M |
| 256 | Dry Forest | 20-30 | M-H | L | L, ML | M | L-M | M |
| 257 | Dry Forest | 20-30 | M-H | L | ML | M | L-M | L-M |
| 258 | Dry Forest | 20-30 | M-H | L | ML | ML-M | L | L-M |
| 265 | Dry Forest | 10-20 | M-H | M | M | M | L-M | M |
| 266 | Dry Forest | 10-20 | VL-M | L,M | VL-M | M | L-M | M |
| 267 | Dry Forest | 20-30 | M-MH | M | M | M | L-M | L-M |
| 268 | Dry Forest | 30-50 | M-H | L,M | M,VL,ML | M | L | L-M |
| 273 | Dry Forest | 20-30 | L-M | M | M | MH | H | M |
| 275 | Dry Forest | 30-50 | L-M | M | M | MH | M-H | M |
| 276 | Dry Forest | 20-30 | VL-M | M | M | MH | M-H | M |
| 277 | Dry Forest | 20-30 | M-MH | M | M | MH | M | M |
| 315 | Dry NonForest | >80 | VL | H | VL | H | H | L |
| 316 | Dry NonForest | >80 | VL | L | VL | MH-H | H | L |
| 317 | Dry NonForest | >80 | VL | M | VL | H | M-H | L |
| 318 | Dry NonForest | >80 | VL | M | VL | MH-H | M | L |
| 326 | Dry NonForest | >80 | VL | M | VL | H | H | L |
| 327 | Dry NonForest | >80 | VL | M | VL | H | M-H | L |
| 332 | Dry NonForest | >80 | VL | M | VL,M | H | L | L |
| 333 | Dry NonForest | >80 | VL | M | VL | H | H | L |
| 356 | Dry NonForest | >80 | VL-L | L | VL | MH | M | L |
| 357 | Dry NonForest | >80 | VL-L | L | VL | MH | M | L |
| 358 | Dry NonForest | >80 | VL | L | VL | MH | L-M | L |
| 365 | Dry NonForest | >80 | VL | M | VL,L | M-H | M-H | L |
| 366 | Dry NonForest | >80 | VL-L | M | VL,L | L-H | M-H | L |
| 367 | Dry NonForest | >80 | VL | M | VL,L | L-H | M | L |
| 368 | Dry NonForest | >80 | VL | L | VL,L | L-H | L-M | L |
| 376 | Dry NonForest | >80 | VL-L | M | VL,L | L-H | M-H | L |
| 377 | Dry NonForest | >80 | VL-M | M | VL L | L-H | M-H | L |
| 416 | Moist NonForest | >50 | VL | M | VL | M-H | H | L |
| 418 | Moist NonForest | >50 | VL | M | VL | M-H | M-H | L |
| 432 | Moist NonForest | >50 | VL | M | VL | MH | M-H | L |
| 433 | Moist NonForest | >50 | VL | M | VL | H | H | L |
| 468 | Moist NonForest | >50 | VL | M | VL,L | H | M-H | L |
| 518 | Rock/Non-Veg | >50 | VL | VL | VL | H | L | L |
| 532 | Rock/Non-Veg | >50 | VL | VL | VL | L | L | L |
| 558 | Rock/Non-Veg | >50 | VL | VL | VL | L | L | L |
| 567 | Rock/Non-Veg | >50 | VL | VL | VL | L | L | L |
| 568 | Rock/Non-Veg | >50 | VL | VL | VL | L | L | L |
| 736 | Non/Dry Forest/Riparian | >80 | VL | M | VL | H | H | L |
| 832 | Very Cold Forest/NonForest | >60 | VL | L | VL | ML-M | L | L |

Management Considerations (Suitability and Limitations)

Table 13 lists the general suitability for and limitations to general forest management practices for each Landtype Association.

Road Construction:  This column rates the suitability for the landscape to support road construction.

SUITABLE (S) - Limitations to road construction are rare or can be mitigated with common construction practices or more expensive construction practices commensurate with the value being accessed by the road.

UNSUITABLE (U) - Limitation to road construction present severe economic constraints and/or severe hazard to ecological processes.  Road construction causing slope instability and/or chronic slope erosion degrading surface water quality and/or reducing site productivity are examples.

Limitation to Road Construction:  Major limitations to road construction are listed.  Similar limitations are listed for both suitable and unsuitable ratings.  When accompanied with a suitable rating, the limitation can be mitigated either by special design, avoidance of feature by alignment, or the limitation by degree is less of a hazard to water quality or site productivity.

Slope stability - High hazard for chronic slope erosion, deep seated landslide, or shallow rapid landslides.

Drainage interception – High amount of seasonal groundwater or high density of channels require special design to manage water intercepted by road.

Sediment delivery – Road likely to deliver road produced sediment directly to a perennial stream or road is likely to be on slopes with high sediment delivery efficiency to a perennial stream.

Clay soil – Regolith has low bearing capacity or ruts easily when wet.

Rock – A high amount of resistant bedrock, talus, and/or boulder fields.

Stream channel – Difficult to avoid road alignment within a channel migration zone.

Cutslope erosion – Regolith erode easily ravelling into road ditches causing high maintenance costs and road drainage failure.

Wetland – Abundant persistently wet areas.

Riparian:  This column identifies which Landtype Associations have a potential for a sizable riparian zone or wetlands within them.  A (Y) in the column denotes “yes”.  An (*) indicates that the riparian zone may occur along the boundary of the map unit.

Limitation to Harvest Operability:  This column lists the degree of limitation to operating ground-base harvest equipment.  The ratings refer to the degree in which landscape features may constrain operability.

LOW (L) – Limitation can be easily mitigated or avoided.   Often the mitigation is restriction of operating season.

MODERATE (M) – Limitations may constrain access to some areas within the LTA or limitations may not be easily mitigated.  Common examples include slope steepness in some areas of the map unit exceed accepted gradient for use of ground-base equipment without impacts to site productivity or fine textured soils remain wet well into the operating season greatly condensing operating season to avoid rutting impacts to site productivity.

HIGH (H) – Limitations are severe and use of ground-base equipment have a high potential for degrading site productivity or pose safety risk to the operator.  Commonly these areas have slope gradients that exceed 60% and/or rock outcrop in most of the map unit.

N/A – Non-forest vegetation indicated and the LTA is not rated.

Operability Limitations:  This column lists the most limiting features to harvest by ground-base equipment.

Access – Road construction limitations severely limits access to the area.

Compaction – Soils have a thick or thin pure volcanic ash mantle that is highly susceptible to compaction.

Riparian – Area has a high potential for wet areas that will either limit access or season of use.

Slope – Areas within the map unit have slope gradients that exceed standard for ground-base equipment harvest.

Rutting/Compaction – Moderately fine and fine textured soils are highly susceptible to rutting and puddling when wet.  These soils retain moisture well into the operating season and are also susceptible to compaction when moist.

Range Suitability – Cattle/Sheep:  These columns list the degree of suitability for grazing management of cattle or sheep.  The rating was determined based upon direction in 36 CFR 219.3 and Forest Service Manual (FSM) 1905.  The following criteria was used to rate suitability for grazing:  < 40% slope gradients for cattle and <60% slope gradients for sheep; < 50% rock outcrop; > 200 lbs/ac clipped dry wt. production, herbage production, and palatability.  The first three criteria was used to determine range capability and the last two criteria were used to rate the degree in which the area was suitable for cattle grazing.

LOW (L) – The area is suitable for grazing; forage values is low.  Either productivity is less than 500 lbs/acre and/or plant palatability is low to moderate.

MODERATE (M) – The area is suitable for grazing; forage values are moderate.  Herbage production ranges from 500 – 1000 lbs/acre and palatability ranges from low to high.

HIGH (H) – The area is suitable for cattle grazing:  forage values are high.  Herbage production ranges from 500- >1000 lbs/acre and palatability is high.

UNSUITABLE (U) – The area is not capable of supporting cattle grazing.  Slope steepness or rock outcrop exceeds standard; and/or forage values are very low with herbage productivity <200 lbs/acre or palatability is very low.

Limitations to Range – Cattle/Sheep:  These columns list the most limit features to range suitability.

Forage – Forage value may be low, either by low herbage production or from low palatability, or both.

Riparian – Stream channels with riparian areas may be a major component of the area.

Seeps – Wet, boggy areas may occur within the LTA map unit.

Slope – A large amount of the area has slopes that exceed the FSM standard of >40% slope gradient for cattle and >60% slope gradient for sheep.

Timber Suitability:  This column lists the rating for suitability of the LTA to support sustainable timber management.  The ratings are based upon provisions in the Forest Management Act (NFMA 16 U.S.C 1604) that define unsuitable lands as those were technology is not available to ensure production without irreversible resource damage to soil or watershed conditions and/or there is no reasonable assurance that lands can be restocked following harvest.

LTA features that assist in predicting the potential to lead to one or both of these conclusions by carrying out timber management are:  1) removal of trees on landforms where tree removal and/or road construction has the potential for accelerated mass wasting or chronic soil erosion that can effect long term site productivity or water quality;  2) site productivity limits stand growth and sustainable timber management is not commercially viable; and 3) removal of trees in environments where site factors limit regeneration within 5 years.  LTA features that have large areas with their map units unsuited for timber management are: steep Landform Groups such as Canyons and Glacial Trough Walls, Cirques, & Alpine Ridges with a high hazard for natural and management-related shallow rapid landslides and accelerated mass wasting; and Vegetation Zones – Parkland, Rock/Non-Vegetated and Dry or Moist Non-Forest which have soil and climatic factors that limit regeneration and forest productivity.

SUITABLE (S) – The area does not contain site factors where timber management using current best management practices and technologies would pose a potential hazard for irreversible resource damage to soil or watershed conditions.  The forest has the potential to regenerate within 5 years given state-of-the-art silvicultural practices suited to site conditions are employed.

UNSUITABLE (U) – Inherent site factors pose a high hazard to irreversible resource damage to soil or watershed conditions or site productivity limits growth to a commercial product or regeneration can not be obtained within 5 years.

Limitations - Timber:  This column lists the most limiting feature to timber management relative to the suitability definition referenced in the previous section.

Forest Productivity – Potential forest productivity is very low; <20 cubic feet/acre/year; e.g., shallow soils.  These areas may not sustain a viable, commercial forest.

Regeneration – Regeneration is severely limited by site factors.  Suitable timber management conditions are those where silvicultural practices can assist seedling establishment e.g., reduction of plant competition by scarification or burning; or provide shade using shelterwood prescriptions.  Unsuitable management conditions are those where site factors are so severe that state-of-the art silvicultural practices are not successful in overcoming inherent site factors to assist seedling establishment.

Slope stability – Mass wasting and/or severe soil erosion processes may be accelerated by tree removal.

Road-Harvest Systems – Slope steepness limits road construction and harvest systems.

Table 13.  Management Considerations – Suitability and Limitation to Forest Practices

| LTA | Road Construct-ion | Road Limitations | Riparian (* stream along map unit edge) | Limitation to Harvest Operability | Limitations - Operability | Range Suitability Cattle | Limitations Cattle | Range Suitability Sheep | Limitations Sheep | Timber Suitability | Limitations - Timber |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |
| 114 | S-U | slope stability | Y | L | compaction | L | forage | L | forage | S | slope stability |
| 115 | S | drainage interception | Y | L | compaction | L | forage | L | forage | S |  |
| 116 | S |  | N | L | compaction | L | forage | L | forage | S |  |
| 117 | S |  | N | M | slope | L | forage, slope | L | forage | S |  |
| 118 | U | slope stability, sediment delivery | Y* | H | slope, access | U | slope | U | slope | S | road-harvest systems |
| 124 | S-U | slope stability, clay soils | Y | M | rutting/ compaction | L | forage | L | forage | S |  |
| 125 | S | drainage interception, clay soils | Y | M | rutting/ compaction | L | forage | L | forage | S |  |
| 126 | S |  | N | M | rutting/ compaction | L | forage | L | forage | S |  |
| 127 | S |  | N | M | slope, rutting/ compaction | L | forage, slope | L | forage | S |  |
| 131 | S |  | Y | L | compaction | L | forage, riparian | L | forage, riparian | S-U | regeneration |
| 132 | U | slope stability, rock, sediment delivery | Y | H | slope, access | U | slope | L | forage, slope | U-S | regeneration, road-harvest systems |
| 133 | U-S | stream channel | Y | L |  | L | forage, riparian | L | forage, riparian | S |  |
| 135 | S |  | Y | L |  | L | forage, riparian | L | forage, riparian | S |  |
| 144 | S-U | slope stability | Y | M | rutting/ compaction | L | forage, seeps | L | forage, seeps | S | slope stability |
| 146 | S-U | slope stability | Y | M | rutting/ compaction | L | forage, seeps | L | forage, seeps | S | slope stability |
| 155 | S | drainage interception | Y | L | compaction | L | forage | L | forage | S |  |
| 156 | S |  | N | L | compaction | L | forage | L | forage | S |  |
| 157 | S |  | N | M | slope | L | forage, slope | L | forage | S |  |
| 158 | U | slope stability, sediment delivery | Y* | H | slope, access | U | slope | U | slope | S |  |
| 165 | S | drainage interception | Y | L | compaction | L | forage | L | forage | S |  |
| 166 | S |  | N | L | compaction | L | forage | L | forage | S |  |
| 167 | S |  | N | M | slope | L | forage, slope | L | forage | S |  |
| 168 | U | slope stability, sediment delivery | Y* | H | slope, access | U | slope | U | slope | S | road-harvest systems |
| 176 | S |  | N | L |  | L | forage | L | forage | S |  |
| 177 | S |  | N | M | slope | L | forage, slope | L | forage | S |  |
| 214 | S-U | slope stability | Y | L | compaction | M | forage, seeps | M | forage, seeps | S | slope stability |
| 215 | S | drainage interception | Y | L | compaction | M | forage, riparian | M | forage, riparian | S |  |
| 216 | S |  | N | L | compaction | M | forage | M | forage | S |  |
| 217 | S |  | N | M | slope | L | forage, slope | M | forage | S |  |
| 218 | U | slope stability, sediment delivery | Y* | H | slope, access | U | slope | U | slope | S | road-harvest systems |
| 224 | S-U | slope stability, clay soils | Y | M | rutting/ compaction | M | forage, seeps | M | forage, seeps | S | slope stability |
| 226 | S | clay soils | Y | M | rutting/ compaction | M | forage, seeps | M | forage, seeps | S |  |
| 227 | S | clay soils, cutslope stability | N | M | slope, rutting/ compaction | L | forage, slope | M | forage | S |  |
| 231 | S |  | Y | L | compaction | M | forage, riparian | M | forage, riparian | S |  |
| 232 | U | slope stability, rock, sediment delivery | Y | H | slope, access | U | slope | L | slope | S-U | regeneration |
| 233 | U-S | stream channel | Y | L | riparian | M | forage, riparian | M | forage, riparian | S |  |
| 236 | S |  | Y | L |  | M | forage, riparian | M | forage, riparian | S |  |
| 244 | S-U | slope stability, clay soils | Y | M | rutting/ compaction | M | forage, seeps | M | forage, seeps | S | slope stability |
| 246 | S | clay soils | N | M | rutting/ compaction | M | forage | M | forage | S |  |
| 256 | S |  | N | L | compaction | M | forage | M | forage | S |  |
| 257 | S | cutslope stability | N | M | slope, compaction | L | forage, slope | M | forage | S |  |
| 258 | U |  | Y* | H | slope, access | U | slope | U | slope | S |  |
| 265 | S | cutslope stability | Y | L |  | M | forage, riparian | M | forage, riparian | S |  |
| 266 | S |  | N | L |  | M | forage | M | forage | S |  |
| 267 | S |  | N | M | slope | L | forage, slope | M | forage | S |  |
| 268 | U | slope stability, sediment delivery | Y* | H | slope, access | U | slope | U | slope | S | road-harvest systems |
| 273 | U-S | stream channel | Y | L |  | M | riparian | M | riparian | S |  |
| 275 | S |  | N | L |  | M | riparian | M | riparian | S |  |
| 276 | S |  | N | L |  | M | forage | M | forage | S |  |
| 277 | S |  | N | M | slope | L | slope | M | forage | S |  |
| 315 | S |  | Y | N/A |  | H |  | H |  | U | forest productivity, regeneration |
| 316 | S |  | N | N/A |  | H |  | H |  | U | forest productivity, regeneration |
| 317 | S | cutslope stability | N | N/A |  | M | slope | H |  | U |  |
| 318 | U | slope stability, sediment delivery | Y | N/A |  | U | slope | U | slope | U | forest productivity, regeneration |
| 326 | S | clay soils | N | N/A |  | H |  | H |  | U | forest productivity, regeneration |
| 327 | S | slope stability, clay soils | N | N/A |  | M | slope | H |  | U | forest productivity, regeneration |
| 332 | U |  | Y | N/A |  | H | riparian | H | riparian | U | forest productivity, regeneration |
| 333 | U-S | stream channel | Y | N/A |  | H | riparian | H | riparian | U | forest productivity, regeneration |
| 356 | S |  | N | N/A |  | H |  | H |  | U | forest productivity, regeneration |
| 357 | S | cutslope stability | N | N/A |  | M |  | H |  | U | forest productivity, regeneration |
| 358 | U | slope stability, sediment delivery | Y* | N/A |  | U | slope | U | slope | U | forest productivity, regeneration |
| 365 | S |  | Y | N/A |  | H | riparian | H | riparian | U | forest productivity, regeneration |
| 366 | S |  | N | N/A |  | H |  | H |  | U | forest productivity, regeneration |
| 367 | S |  | N | N/A |  | M | slope | H |  | U | forest productivity, regeneration |
| 368 | U | slope stability, sediment delivery | Y* | N/A |  | U | slope | U | slope | U | forest productivity, regeneration |
| 376 | S |  | N | N/A |  | H |  | H |  | U | forest productivity, regeneration |
| 377 | S |  | N | N/A |  | M | slope | H |  | U | forest productivity, regeneration |
| 416 | S |  | N | N/A |  | L |  | L |  | U | forest productivity, regeneration |
| 418 | U | slope stability, sediment delivery | N | N/A |  | U | slope | U | slope | U | forest productivity, regeneration |
| 432 | U | slope stability, rock, sediment delivery | Y | N/A |  | U | slope | U | slope | U | forest productivity, regeneration |
| 433 | U | wetlands | Y | N/A |  | L | riparian | L | riparian | U | forest productivity, regeneration |
| 468 | U | slope stability, sediment delivery | Y* | N/A |  | U | slope | U | slope | U | forest productivity, regeneration |
| 518 | U | slope stability, rock, sediment delivery | N | H |  | U | rock, slope | U | rock, slope | U | forest productivity, regeneration |
| 532 | U | slope stability, sock, sediment delivery | N | N/A |  | U | rock, slope, short season | L-M | rock, slope, short season | U | forest productivity, regeneration |
| 558 | U | slope stability, sock, sediment delivery | Y | H | slope, access | U | rock, slope | U | rock, slope | U | forest productivity, regeneration |
| 567 | U | rock |  | H | slope, access | U | rock, slope | L | rock, slope | U | forest productivity, regeneration |
| 568 | U | slope stability, rock, sediment delivery | Y* | H | slope, access | U | slope | U | slope | U | forest productivity, regeneration |
| 736 | S | cutslope stability | Y | H | slope, access | M | riparian | M | riparian | U | forest productivity, regeneration |
| 832 | U | rock, slope stability | N | N/A |  | U | slope | L-M | rock, slope, short season | U | forest productivity, regeneration |

Natural Disturbance Regimes

Table 15 contains the Natural Disturbance Regimes for each Landtype Association.  Listed below is a brief description of the information contained in each column of the table.

Hydrologic Event:  Three types are identified as most likely to cause a channel response or flood.  They are late fall/winter rain-on-snow; high intensity convective storms; and rapid spring snowmelt.  These events do not occur in all Landtype Associations, they occur in some regions and not in others within the same Landtype Association, and the event can vary with elevation.  Rain-on-snow is very uncommon and may not be easily distinquished from rapid snowmelt periods.  High intensity convective storms occur during late spring and early summer and are very difficult to predict.  They are local in extent covering one to several subwatersheds per event and are often generated by local or regional orographic effects.  This table assumes the possibility of convective storms as a disturbing agent throughout the Blue Mountain ecoregion.  A significant event can occur with rapid spring snowmelt, particularly when the ground is still frozen or when combined with spring rains.

Hydrologic Response:  The table lists dominant geomorphic and hydrologic processes that are affected by the hydrologic event that can lead to a predicted channel response.  Road drainage failures have been noted for those Landtype Associations where stream density is high or has a convergent pattern that accelerates runoff events.

Wind Event Response:  The table lists an interpretation for potential response of mature forests to high wind events.  Tree topple by wind is an important disturbance as it creates habitat features important to several wildlife species and effects movement of other species.  The potential for wind topple influences selection of silvicultural practices and timber management programs.  Frequency and location of wind disturbance may be higher in some locations due to orographic effects not predicted by the survey.  This interpretation assumes the same potential for wind event across the landscape and a mature forest.  The criteria used to develop the interpretation are: soil depth, bedrock hardness and resistance to root penetration, and topographic position of the LTA within the landscape setting.  These relationships have been observed in the field during soil survey mapping in 1997 and 1998.

LOW – The LTA has deep soils and/or is located in a valley floor position which reduces the potential for tree topple from wind.  Potential for stand level disturbance is low; isolated trees may fall but usually as a result of another initial disturbance agent, i.e., insect/disease.

MODERATE – The LTA has deep to moderately deep soils, is in a mid landscape position, and/or have hard, resistant bedrock.  A severe windstorm could cause patches of trees to topple but the chance of stand-wide topple is low.

HIGH – The LTA has shallow to moderately deep soils, is on a summit or backslope position, and has hard, resistant bedrock or has tree species susceptible wind (engleman spruce) on seasonally wet soils.  A severe windstorm may topple numerous trees in the stand causing “jack-strawed” understories.

Variable – The LTA is variable and man conditions exist which may present a range of potential for wind topple.

n/a – The LTA is dominantly non-forest or has inclusions of open-grown forest and was not rated.

Fire Regime Disturbance (Historical):  This column lists the numeric or alphanumeric code associated with historic fire regimes as defined by Lueschen (2000) in Fire Regimes of Oregon and Washington.  This interpretation is limited to historical fire disturbance in an unmanaged setting.  Fire regimes were applied to each LTA based upon the most dominant potential natural vegetation (PNV) or vegetation zone for the LTA.  In some cases, PNV was combined with landform groups when terrain features uniquely influences distribution patterns of potential natural vegetation or frequency of fire.  A table is provided below that describes fire frequency and severity and outlines the criteria for each fire regime code used in Lueschen (2000).  In addition, this table includes a relative rating for each fire regime as it may affect vegetation communities either directly or indirectly.

It is widely accepted that most forest communities in the Interior Columbia Basin evolved and were maintained under various fire regimes.  This interpretation is useful in comparing historical patterns of fire disturbance with today’s existing or potential fire regimes given the additional information on existing vegetation structure or current fire incidence is known.  According to research conducted from the Wenatchee Sciences Lab, historic fire regimes began to change approximately 100 years ago with the onset of forest management.  Past management activities including grazing, vegetation manipulation, fire suppression have altered vegetation structure which can alter natural fire regimes (Everett, Schellhaas, Keenum, Spurbeck, and Ohlson [undated draft]).  The effect of altered natural fire regimes is of concern to management and is currently being studied.

On the next page is a table illustrating the fire regime categories with an interpretation relating fire severity and frequency to degree of disturbance and response.

Table 14.  Fire Regimes of Oregon and Washington (Lueschen 2000) and Relative Disturbance and Response in LTAs

| Code | Frequency and Severity | Plant Communities and Fire Regime Description | Relative disturbance and response in LTAs |
| --- | --- | --- | --- |
| I | 0-35 years, Low Severity | Typical potential plant communities include ponderosa pine, eastside/dry Douglas fir, pine-oak woodlands, Jeffery pine on serpentine soils, oak woodlands, and very dry white fir. Large stand-replacing fire can occur under certain weather conditions, but are rare events (i.e. every 200+ years). | VERY LOW – Low severity fire was likely a major contributor to nutrient cycling; converting forest floor to available nutrients. Frequent historic fire intervals kept fuels from accumulating that would have caused higher severity. Natural wood debris would have ranged from 5-15 tons/acre (Graham 1994). Forest floor duff layers ranged from non-existent to no more than one inch depth. |
| II | 0-35 years, Stand-replacing, non-forest | Typical potential plant communities includes true grasslands and savannahs with typical fire return intervals of less than 10 years; mesic sagebrush communities with typical fire return intervals of 25-35 years up to 50 years, and mountain shrub communities (e.g., bitterbrush, snowberry, ninebark, ceanothus, Oregon chaparral) with fire return intervals of 10-25 years. Fire severity is generally high to moderate; grasses and fire-tolerant shrubs are not completely killed and usually resprout. | LOW – Effects from natural fires were probably low as most fires occurred in late summer when vegetation was semi-dormant from drought. Downed woody debris was localized and less than 5 tons/acre. Forest floor duff layers ranged from non-existent to over two inches in depth depending on fire frequency. |
| III | 35-100+ years, Mixed Severity | This regime results in heterogeneous plant communities and includes several communities as described in subcategories “a-c” below. Large, stand-replacing fires may occur but are usually rare events. Such stand-replacing fires may “reset” large areas but subsequent mixed intensity fires are important for creating heterogeneity. Within this regime, stand structure and composition is not dominated by one or two age classes. | MODERATE – Effects from a range of non-lethal to lethal fire causes a diversity of disturbances. Downed woody debris would have been somewhat common and accumulations ranged from 10-15 tons/acre. Mixed severity fires causing some tree mortality would have contributed to cycling of down woody debris. Forest floor duff layers ranged from 0.5 to 1.0 inch depending on fire intervals. Thicker duff layers would have been maintained with lower frequency fire returns. |
| IIIa | <50 years, Mixed Severity | Typical potential plant communities include mixed conifer, very dry westside Douglas-fir, and dry grand fir. Lower severity fire tends to predominate in many events. |  |
| IIIb | 50-100 years, Mixed Severity | Typical potential plant communities include well drained western hemlock; warm, mesic grand fir, particularly east of the Cascade crest; and eastside western redcedar. The relative amount of lower and higher severity patches within a given event is intermediate between IIIa and IIIc. |  |
| IIIc | 100-200 years, Mixed Severity | Typical potential plant communities include western hemlock, Pacific silver fir, and whitebark pine at or below 45 degrees latitude and cool, mesic grand fir and Douglas-fir. Higher severity fire tends to dominate in many events. |  |
| IV | 35-100+ years, Stand-replacing | Typical potential plant communities are those where seral communities are maintained by stand replacing fires. Seral communities are comprised of Lodgepole pine, aspen, western larch, and western white pine. Dry sagebrush communities also fall within this fire regime. (Natural ignitions within this regime resulting in large fires may be relatively rare). This category is separated into subcategories having different potential climax plant communities. | HIGH – High severity fire is common with a variety of short term and long term effects to soils and forest structure. Highly variable patterns of age class and density is somewhat controlled by fire extent and regeneration response on different slope gradients and aspects. Downed woody debris would have been common and may have been extensive |
| IVa | 35-100+ years, Stand-replacing, Juxtaposed | Typical potential plant communities are located upslope from a plant community with a shorter fire regime interval. The community experiences a shorter fire interval that would be expected due to association with a plant community with a more frequent fire interval downslope. Examples include Lodgepole pine immediately above ponderosa pine in the eastside Washington Cascades and aspen imbedded within dry grand fir in the Blue Mountains. This regime is often found in lower elevations or drier sites than is considered typical for regime IV. | as a result of tree mortality. “Reburns’ in areas of high debris accumulation would have reduced fuel levels and caused severe heating of soils and removal of duff layers. Down woody debris average range may have been 15-25 tons/acre (Graham 1994) or higher and forest floor duff layers ranged from 0.5 to 1.5 inches depending on severity and frequency. |
| IVb | 100+ years, Stand-replacing, Patchy arrangement | Typical potential communities include subalpine fir and mountain hemlock parkland and whitebark pine north of 45 degrees latitude. |  |
| IVc | 100-200 years, Stand-replacing | Typical forest communities include subalpine mixed conifer (e.g., spruce-fir), western larch, and western white pine. Important potential plant communities include mountain hemlock in the Cascades and Pacific silver fir north of 45 degrees latitude. |  |
| V | >200 years, Stand-replacing | This fire regime occurs at the environmental extremes where natural ignitions are very rare or virtually non-existent or environmental conditions rarely result in large fires. Sites tend to be very cold, very hot, very wet, very dry or some combination of these conditions. | VERY HIGH – High severity fire in plant communities less adapted to fire disturbance. Downed woody debris would have been abundant and often exceeded 30 tons/acre (Graham 1994). Coarse woody debris would have substantially contributed to biomass of forest floor duff layers. Duff layers often exceeded 2 inches and were composed of approximately 50 percent decaying wood. After fire, these characteristics would be reset. |
| Va | 200-400 years, Stand-replacing | Plant communities are somewhat fire adapted. Typical communities include Douglas-fir, noble fir, and mountain hemlock on drier sites in western Washington. |  |
| Vb | 400_ years, Stand-replacing | Plant communities are less fire adapted. Typical plant communities include Douglas-fir, Pacific silver fir, western hemlock western redcedar, and mountain hemlock on moister sites in western Washington. |  |
| Vc | No Fire | Plant communities have no evidence of fire for 500+ years. Typical plant communities include Sitka spruce, Pacific silver fir and very wet western redcedar sites. | NONE – Natural fire of any extent is uncommon. |
| Vd | Non-forest | Typical plant communities include black sagebrush, salt desert scrub, alpine communities, and subalpine heath. Most species tend to be small and low growing. Bare ground is common. |  |

Table 15.  Natural Disturbance Regimes and Responses

| LTA | Hydrologic_Event | Hydrologic_Response | Wind Event_Response | Fire Regime | Resonse to Fire |
| --- | --- | --- | --- | --- | --- |
| 114 | High stream flows | Stream erosion along margins initiates landslide | Variable | IIIb, IIIc, IV | Moderate-High |
| 115 | Convective Storm/Rapid Snowmelt | Colluvial stream downcutting; road drainage failures | Moderate | IIIb, IV | Moderate-High |
| 116 | Convective Storm/Rapid Snowmelt | Overland flow and ponding | High | IIIb, IV | Moderate-High |
| 117 | Convective Storm/Rapid Snowmelt | Colluvial stream downcutting; road drainage failures | Moderate | IIIb, IV | Moderate-High |
| 118 | Convective Storm/Rapid Snowmelt | Shallow rapid landslides | Moderate | IIIb, IVa | Moderate-High |
| 124 | High stream flows | Stream erosion along margins initiates landslide | Variable | IIIb | Moderate |
| 125 | Convective Storm/Rapid Snowmelt | Colluvial stream downcutting; road drainage failures | Moderate | IIIb | Moderate |
| 126 | Convective Storm/Rapid Snowmelt | Overland flow and ponding | Moderate | IIIb | Moderate |
| 127 | Convective Storm/Rapid Snowmelt | Colluvial stream downcutting; road drainage failures | Moderate | IIIb | Moderate |
| 131 | Rapid Snowmelt/High stream flows | Stream channel migration | Moderate-High | IIIc, Ivc | Moderate-High |
| 132 | Convective Storm/Rapid Snowmelt | Shallow rapid landslides, snow avalanche | Variable | IVc | High |
| 133 | High stream flows | Stream channel migration | Low | IVc | High |
| 135 | Convective Storm/Rapid Snowmelt | Colluvial stream scour/fan deposition; road drainage failures | Low | IVc | High |
| 144 | Convective Storm/Rapid Snowmelt | Stream at margin undercuts slope or groundwater initiates landslide | Variable | IIIb, IIIc, IV | Moderate-High |
| 146 | Convective Storm/Rapid Snowmelt | Overland flow and ponding; landslide | Low | IIIb, IIIc, IV | Moderate-High |
| 155 | Convective Storm/Rapid Snowmelt | Colluvial stream scour/fan deposition; road drainage failures | Moderate | IV | High |
| 156 | Convective Storm/Rapid Snowmelt | Overland flow | Moderate | IV | High |
| 157 | Convective Storm/Rapid Snowmelt | Colluvial stream downcutting; road drainage failures | Moderate | IV | High |
| 158 | Convective Storm/Rapid Snowmelt | Shallow rapid landslides | Moderate | IIIb, IV | Moderate-High |
| 165 | Convective Storm/Rapid Snowmelt | Colluvial stream scour/fan deposition; road drainage failures | Moderate | IV | High |
| 166 | Convective Storm/Rapid Snowmelt | Overland flow | Moderate | IIIb, IV | Moderate-High |
| 167 | Convective Storm/Rapid Snowmelt | Colluvial stream downcutting; road drainage failures | Moderate | IIIb, IV | Moderate-High |
| 168 | Convective Storm/Rapid Snowmelt | Shallow rapid landslides | Moderate | IIIb, IV | Moderate-High |
| 176 | Convective Storm/Rapid Snowmelt | Overland flow | Moderate-High | III, IV | Moderate-High |
| 177 | Convective Storm/Rapid Snowmelt | Colluvial stream downcutting; road drainage failures | Moderate | III, IV | Moderate-High |
| 214 | High stream flows | Stream erosion along margins initiates landslide | Variable | III | Moderate |
| 215 | Convective Storm/Rapid Snowmelt | Colluvial stream downcutting; road drainage failures | Moderate | III | Moderate |
| 216 | Convective Storm/Rapid Snowmelt | Overland flow and ponding | High | III | Moderate |
| 217 | Convective Storm/Rapid Snowmelt | Colluvial stream downcutting; road drainage failures | Moderate | III | Moderate |
| 218 | Convective Storm/Rapid Snowmelt | Shallow rapid landslides,accelerated erosion | Moderate | III | Moderate |
| 224 | High stream flows | Stream erosion along margins initiates landslide | Variable | III | Moderate |
| 226 | Convective Storm/Rapid Snowmelt | Overland flow and ponding; gully erosion | Moderate | III | Moderate |
| 227 | Convective Storm/Rapid Snowmelt | Colluvial stream downcutting; road drainage failures | Moderate | III | Moderate |
| 231 | Rapid Snowmelt | Stream channel migration | Moderate | IIIc | Moderate |
| 232 | Convective Storm/Rapid Snowmelt | Shallow rapid landslides, snow avalanche | Moderate | III | Moderate |
| 233 | High stream flows | Stream channel migration | Low | IIIc | Moderate |
| 236 | Convective Storm/Rapid Snowmelt | Overland flow | Low | IIIc | Moderate |
| 244 | Convective Storm/Rapid Snowmelt | Stream erosion along margins or groundwater initiates landslide | Variable | III | Moderate |
| 246 | Convective Storm/Rapid Snowmelt | Overland flow and ponding; landslide | Low | III | Moderate |
| 256 | Convective Storm/Rapid Snowmelt | Overland flow and ponding | Moderate | III | Moderate |
| 257 | Convective Storm/Rapid Snowmelt | Colluvial stream downcutting; road drainage failures | Moderate | III | Moderate |
| 258 | Convective Storm/Rapid Snowmelt | Shallow rapid landslides, accelerated erosion | Moderate | III | Moderate |
| 265 | Convective Storm/Rapid Snowmelt | Colluvial stream scour/fan deposition; road drainage failures | Low | III | Moderate |
| 266 | Convective Storm/Rapid Snowmelt | Overland flow and ponding | Moderate | III | Moderate |
| 267 | Convective Storm/Rapid Snowmelt | Colluvial stream downcutting; road drainage failures | Moderate | III | Moderate |
| 268 | Convective Storm/Rapid Snowmelt | Shallow rapid landslides | Moderate | III | Moderate |
| 273 | High stream flows | Stream channel migration | Low | IIIc | Moderate |
| 275 | Convective Storm/Rapid Snowmelt | Colluvial stream downcutting; road drainage failures | Low | III | Moderate |
| 276 | Convective Storm/Rapid Snowmelt | Overland flow | Moderate | III | Moderate |
| 277 | Convective Storm/Rapid Snowmelt | Colluvial stream downcutting; road drainage failures | Moderate | III | Moderate |
| 315 | Convective Storm/Rapid Snowmelt | Colluvial stream scour/fan deposition; road drainage failures | n/a | I, II | Very Low-Low |
| 316 | Convective Storm/Rapid Snowmelt | Overland flow | n/a | I, II | Very Low-Low |
| 317 | Convective Storm/Rapid Snowmelt | Overland flow | n/a | I, II | Very Low-Low |
| 318 | Convective Storm/Rapid Snowmelt | Shallow rapid landslides, accelerated erosion | n/a | I, II | Very Low-Low |
| 326 | Convective Storm/Rapid Snowmelt | Overland flow and ponding | n/a | I, II | Very Low-Low |
| 327 | Convective Storm/Rapid Snowmelt | Colluvial stream downcutting; road drainage failures | n/a | I, II | Very Low-Low |
| 332 | Convective Storm/Rapid Snowmelt | Shallow rapid landslides, snow avalanche, accelerated erosion | n/a | V, Vd | Very High |
| 333 | High stream flows | Stream channel migration | n/a | I, II | Very Low-Low |
| 356 | Convective Storm/Rapid Snowmelt | Overland flow | n/a | I, II | Very Low-Low |
| 357 | Convective Storm/Rapid Snowmelt | Colluvial stream downcutting; road drainage failures | n/a | I, II | Very Low-Low |
| 358 | Convective Storm/Rapid Snowmelt | Shallow rapid landslides, accelerated erosion | n/a | I, II | Very Low-Low |
| 365 | Convective Storm/Rapid Snowmelt | Colluvial stream downcutting; road drainage failures | n/a | I, II | Very Low-Low |
| 366 | Convective Storm/Rapid Snowmelt | Overland flow | n/a | I, II | Very Low-Low |
| 367 | Convective Storm/Rapid Snowmelt | Colluvial stream downcutting; road drainage failures | n/a | I, II | Very Low-Low |
| 368 | Convective Storm/Rapid Snowmelt | Shallow rapid landslides, accelerated erosion | n/a | I, II | Very Low-Low |
| 376 | Convective Storm/Rapid Snowmelt | Overland flow | n/a | I, II | Very Low-Low |
| 377 | Convective Storm/Rapid Snowmelt | Colluvial stream downcutting; road drainage failures | n/a | I, II | Very Low-Low |
| 416 | Convective Storm/Rapid Snowmelt | Overland flow | n/a | I, II | Very Low-Low |
| 418 | Convective Storm/Rapid Snowmelt | Shallow rapid landslides | n/a | I, II | Very Low-Low |
| 432 | Convective Storm/Rapid Snowmelt | Shallow rapid landslides, snow avalanche | n/a | I, II | Very Low-Low |
| 433 | High stream flows | Stream channel migration | n/a | I, II | Very Low-Low |
| 468 | Convective Storm/Rapid Snowmelt | Shallow rapid landslides | n/a | I, II | Very Low-Low |
| 518 | Convective Storm/Rapid Snowmelt | Shallow rapid landslides | n/a | V, Iva | High-Very High |
| 532 | Convective Storm/Rapid Snowmelt | Shallow rapid landslides, snow avalanche | n/a | V, Iva | High-Very High |
| 558 | Convective Storm/Rapid Snowmelt | Shallow rapid landslides | n/a | V, Iva | High-Very High |
| 567 | Convective Storm/Rapid Snowmelt | Accelerated erosion | n/a | V, Iva | High-Very High |
| 568 | Convective Storm/Rapid Snowmelt | Accelerated erosion | n/a | V, Iva | High-Very High |
| 736 | Convective Storm/Rapid Snowmelt | Colluvial stream downcutting; road drainage failures | n/a | I, III | Very Low - Moderate |
| 832 | Convective Storm/Rapid Snowmelt | Shallow rapid landslides, snow avalanche, accelerated erosion | n/a | Ivb | High |

# Comments

Page: 29
There are no occurrences of “minor influence” of volcanic ash; in contrast to several map units in table 8 that are dominantly “minor” ash influence. Why the discrepancy?

Page: 36
There is a problem with this definition. Surface texture is usually undertood to be texture of the surface horizon (e.g. A, E horizons). The root zone usually extends into subsurface B horizons and often into C horizon substratum. The root zone extends to a bedrock contact in many soils that are less than 60 inches deep. These soils would not have a “regolith”. I assumed you determined surface texture and regolith texture from family particle-size (e.g. ashy over clayey-skeletal). If this is not really texture of the surface horizon, I propose we name it something other than “surface texture” (e.g. Upper Regolith Texture) to avoid confusion.